## Slide 1
1 Introduction

## Slide 2: Highlights
Uses of Computer Networks
Network Hardware
Network Software
Reference Models
Example Networks
Network Standardization

## Slide 3: Computer Networks
Computer Networks
  A collection of autonomous computers interconnected by a single technology
  Users are exposed to the actual machines
  If the machines have different hardware and different operating systems, that is fully visible to the users

## Slide 4: Distributed system
Distributed system
  A collection of independent computers appears to its users as a single coherent system
  A layer of software on top of the operating system, called middleware, is responsible for implementing this model
  A well-known example of a distributed system is the World Wide Web, in which everything looks like a document (Web page)

## Slide 5: Definition of Computer Networks
Components of CN
  Computers/Hosts/End Systems
  Communication Links
  Switches/Routers
Notes: End System(host): Computing Devices 不仅是计算机（台式机/笔记本），还有PDA、手机、电视、家用电器、汽车、传感设备、Web相机、数字相框…
类比：交通网络
如100台电视要使用2辆卡车从广东的厂家运到北京国美商场
Host: 建筑物，
Packets：卡车，每辆车独立运送
Links: 铁路、公路
Switch：立交桥
Application/Services: Email, Web surfing, Instant Messaging(QQ), Streaming Video(土豆网)，VoIP…

## Slide 6
1.1 Uses of Computer Networks

## Slide 7
Business Applications

## Slide 8: Resource Sharing
Sharing physical resources
  Printers
  Scanners
  CD burners
Sharing computerized information
  Database
  Documents

## Slide 9: Client-Server Model
A network with two clients and one server
Notes: 服务器存储资源、提供服务（应用）

## Slide 10: Communication Medium
E-mail
Makes cooperation among far-flung groups of people easy
Videoconferencing
Notes: far-flung adj
1) long distance away 遥远的
expeditions to the far-flung corners of the world 去世界偏远地方的探险
2) spread over a wide area 分布广的；广泛的

## Slide 11: Electronic Commerce
Doing business electronically with other companies, especially suppliers and customers
  Reduces the need for large inventories and enhances efficiency
Doing business with consumers over the Internet
  Airlines, bookstores, and music vendors …
Notes: Enterprise Resource Planning
B-B
B-C
C-C

## Slide 12
Home Network Applications

## Slide 13: Access to remote information
Surfing the World Wide Web for information
Newspapers, magazines, scientific journals
On-line digital library

## Slide 14: Person-to-person communication
Instant messaging
Chat room
Newsgroups
Peer-to-peer system
Carry telephone calls, video phone, radio
Notes: P2P: 没有固定的客户/服务器角色

## Slide 15: Interactive entertainment
Video on demand
Game playing

## Slide 16: E-commerce
Some forms of e-commerce

## Slide 17
Mobile Network Users

## Slide 18: Mobile Network Users
Combinations of wireless networks and mobile computing.
Notes: 家庭无线LAN
手机上网

## Slide 19: Mobile Network Users
Portable office
Trucks, taxis, …, keeping in contact with home
Meter reading
RFID
Notes: Radio Frequency Identification电子标签，无接触识别
可承载比条形码更丰富的信息，例如商品货号、生产日期、到库日期…

## Slide 20
Social Issues

## Slide 21
1.2 Network Hardware

## Slide 22
Transmission technology and scale

## Slide 23: Transmission technology
Broadcast networks
  Sending a packet to all destinations, each machine checks the address field
    If the packet is intended for the receiving machine, that machine processes the packet
    If the packet is intended for some other machine, it is just ignored.
  Broadcasting
  Multicasting (subscribe)
Point-to-point networks
  To go from the source to the destination, a packet may visit one or more intermediate machines (Often multiple routes are possible, finding good ones is important)

## Slide 24: Broadcast vs. Point-to-point
A broadcast network
A point-to-point network

## Slide 25: Classification by scale

## Slide 26: PAN

## Slide 27
Local Area Networks

## Slide 28: Topology
Two broadcast networks
(a) Bus
(b) Ring

## Slide 29: 802.11/Switched LAN

## Slide 30: Channel allocation
Static & Dynamic
A typical static allocation
  Divide time into discrete intervals and use a round-robin algorithm, allowing each machine to broadcast only when its time slot comes up
Dynamic allocation methods
  Centralized
  Decentralized

## Slide 31
MAN and WAN

## Slide 32: Metropolitan Area Networks
A metropolitan area network based on cable TV

## Slide 33: WAN
WAN: telecommunication network that covers a broad area
Providing connections from a LAN to the Internet

## Slide 34: Communication subnet
Transmission lines
Switching elements (Router)
  Store-and-forward (packet-switched)
  reassembled
  Routing decisions: Routing algorithm

## Slide 35
Wireless Networks

## Slide 36: Categories of wireless networks
System interconnection
  Bluetooth
  In the simplest form, system interconnection networks use the master-slave paradigm
Wireless LANs(802.11-WiFi)
Wireless MANs(802.16 WiMax)
Wireless WANs

## Slide 37
Internetworks

## Slide 38: Internet & internet
A collection of interconnected networks is called an internetwork or internet
  Gateway: provide the necessary translation, both in terms of hardware and software
The worldwide Internet (which is one specific internet)
[J. Kurose]

## Slide 39: Subnet, Network, internet
Subnet
  The collection of routers and communication lines
Network
  The combination of a subnet and its hosts forms a network
internetwork
  An internetwork is formed when distinct networks are interconnected

## Slide 40
1.3 Network Software

## Slide 41
Protocol Hierarchies

## Slide 42: Network architecture
Networks are organized as a stack of layers
  Reduce design complexity
  The purpose of each layer is to offer certain services to the higher layers, shielding those layers from the details of how the offered services are actually implemented
  Each layer is a kind of virtual machine, offering certain services to the layer above it
Object-oriented programming
  A particular piece of software (or hardware) provides a service to its users but keeps the details of its internal state and algorithms hidden from them
Notes: Networks are complex!
many “pieces”:hosts, routers, links of various media, applications, protocols. hardware, software
Question: Is there any hope of organizing structure of network?

## Slide 43: Layers, Peers, Protocols, and Interfaces

## Slide 44: Layers, protocols, and interfaces
Protocol
  An agreement between the communicating parties on how communication is to proceed
Peers
  The entities comprising the corresponding layers on different machines are called peers
  The peers may be processes, hardware devices
Physical medium
Interface
  Defines which primitive operations and services the lower layer makes available to the upper one
Network architecture
  A set of layers and protocols
  Neither the details of the implementation nor the specification of the interfaces is part of the architecture

## Slide 45: Philosopher-Translator-Secretary
Interfaces
Protocols
  Translator: A neutral language known to both of them
  Secretary: communication method

## Slide 46: Information flow
Example information flow supporting virtual communication in layer 5.
Notes: 类比：A公司北京总部人事部的Alice想要给南京分公司网络部的Bob发送一份工资单（Layer 5 Message），这个通知装在公司内部信封中，上面有Bob的部门和名字（Layer 4 Message），行政助理将这个信封装在统一的邮政信封中，并写上南京分公司的地址和北京总公司的地址（Layer 3 Message）, 邮局将邮政信封发到南京分公司，行政助理接收，拆开，将内部信封交给Bob；Bob打开信封，看到工资单。

## Slide 47: Virtual Communication of Layer 5 Peers(1)
Layer 5
  A message, M, is produced by an application process and given to layer 4 for transmission
Layer 4
  Puts a header in front of the message to identify the message and passes the result to layer 3
  Header: control information, such as sequence numbers (In some layers, headers can also contain sizes, times, and other control fields)

## Slide 48: Virtual Communication of Layer 5 Peers(2)
Layer 3
  There is limit to the size of messages transmitted in the layer 3 protocol
  Break up the incoming messages into smaller units (packets)
  Prepend a layer 3 header to each packet
  Decides which of the outgoing lines to use and passes the packets to layer 2
Layer 2
  Adds a header & trailer to each piece
  Gives the resulting unit to layer 1
Layer 1
  Physical transmission

## Slide 49: A Practical Case
message
segment
datagram
frame
source
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
Hl
M
router
switch

## Slide 50
Design Issues for the Layers

## Slide 51: Design Issues for the Layers
Reliability
  Error detection and error correction
  Routing: find a path through a netwrok
Network evolution
  Protocol layering
  Addressing or naming: identifying senders and receivers
  Internetworking（网络互通性）
  Scalability(可扩展性)
Resource allocation
  Statistical multiplexing（统计复用：按需分配）
  Flow Control(流量控制)
QoS（服务质量）
Security

## Slide 52: Error Control
Physical lines are not perfect
  Error-detecting & Error-correcting codes
  How the receiver tells the sender which messages have been correctly received and which have not
Messages may be out of sequence
  How the sender numbers the messages
  How the receiver deals with the messages arriving out of order

## Slide 53: Addressing
Each layer needs a mechanism for identifying senders and receivers
  Sender: a process on a machine
  Receiver: a process on another machine

## Slide 54: Flow Control
A fast sender may swamp a slow receiver with data
  Method 1: some kind of feedback from the receiver to announce it’s current situation
  Method 2: limit the sender’s transmission rate

## Slide 55: Routing
When multiple paths exist, a route must be chosen

## Slide 56
Service Primitives

## Slide 57: Connection-Oriented and Connectionless Services
Six different types of service
Connection-oriented: telephone system
Connection-less: postal system

## Slide 58: Interfaces and services
Service provider and service user
  The entities in layer n implement a service used by layer n+1, layer n is called the services provider, layer n+1 is called service user
SAP: Service Access Point
  Layer n SAPs are the places where layer n+1 can access the services offered
PDU: Protocol Data Unit
  Information exchanged between two peers

## Slide 59: Service Primitives
A service is formally specified by a set of primitives (operations) available to a user process to access the service
Example
  CONNECT.request - request a connection to be established
  CONNECT.indication - signal the called party
  CONNECT.response - used by the called to accept/reject calls
  CONNECT.confirm – tell the caller whether the call was accepted
  DATA.request – request that data be sent
  DATA.indication – signal the arrival of data
  DISCONNECT.request – request that a connection be released
  DISCONNECT.indication – signal the peer about the request

## Slide 60: Service Primitives: Example
  1. CONNECT.request
  2. CONNECT.indication
  3. CONNECT.response
  4. CONNECT.confirm
  5. DATA.request
  6. DATA.indication
  7. DATA.request
  8. DATA.indication
  9. DISCONNECT.request
  10.DISCONNECT.indication

## Slide 61: A Simple Connection-oriented Service
If the protocol stack is located in the operating system, the primitives are normally system calls
Five service primitives for implementing a simple connection-oriented service.

## Slide 62: A Simple Connection-oriented Service
Packets sent in a simple client-server interaction on a connection-oriented network.

## Slide 63: The Relationship of Services to Protocols
Service
  Defines what operations the layer is prepared to perform on behalf of its users, but it says nothing at all about how these operations are implemented
  Relates to an interface between two layers, with the lower layer being the service provider and the upper layer being the service user
Protocol
  A set of rules governing the format and meaning of the messages that are exchanged by the peer entities
  Entities use protocols to implement their service definitions
Service and protocol are completely decoupled
  They are free to change their protocols provided they do not change the service

## Slide 64: The Relationship of Services to Protocols

## Slide 65
1.4 Reference Models

## Slide 66
The OSI Reference Model

## Slide 67: The OSI reference model

## Slide 68: Physical layer
Transmitting raw bits over a communication channel
  how many volts should be used to represent a 1 and how many for a 0
  how many nanoseconds a bit lasts
  whether transmission may proceed simultaneously in both directions
  how the initial connection is established and how it is torn down when both sides are finished

## Slide 69: Data link layer
Transform a raw transmission facility into a logic channel (Point-to-Point: the protocols are between each machine and its immediate neighbors)
  Sender break up the input data into data frames and transmit the frames
  If the service is reliable, the receiver confirms correct receipt of each frame by sending back an acknowledgement frame
  Flow control: Keep a fast transmitter from drowning a slow receiver in data
  Broadcast networks: how to control access to the shared channel

## Slide 70: Network layer
Controls operation of subnet
  Forwarding
  Routing: How packets are routed from source to destination (route table)
    Static
    Be determined at start of each conversation
    Highly dynamic
  Congestion
  QoS (Quality of service)
    delay, transit time, jitter, etc.
  Heterogeneous networks interconnection
  Broadcast networks, routing is simple

## Slide 71: Transport Layer
Transport Layer: end-to-end layer
  Accept data from above, split it up into smaller units if need be, pass these to the network layer, and ensure that the pieces all arrive correctly at the other end
  Determines what type of service to provide to the session layer
    an error-free end-to-end channel
    transporting of isolated messages, with no guarantee about the order of delivery
    broadcasting of messages to multiple destinations

## Slide 72: Session Layer
The session layer allows users on different machines to establish sessions
Dialog control
  keeping track of whose turn it is to transmit
Token management
  preventing two parties from attempting the same critical operation at the same time
Synchronization
  checkpointing long transmissions to allow them to continue from where they were after a crash

## Slide 73: Presentation Layer
The syntax and semantics of the information transmitted
  the data structures to be exchanged can be defined in an abstract way

## Slide 74: Application Layer
Application layer contains a variety of protocols that are commonly needed by users.
  HTTP (HyperText Transfer Protocol)
  File transfer
  Electronic mail
  Network news
  …….

## Slide 75
The TCP/IP Reference Model

## Slide 76: The TCP/IP Reference Model

## Slide 77: The Internet Layer
A packet-switching network based on a connectionless internetwork layer
Defines an official packet format and protocol called IP (Internet Protocol)
The job of the internet layer is to deliver IP packets where they are supposed to go
  Packet routing
  Avoiding congestion

## Slide 78: The Transport Layer: TCP
TCP (Transmission Control Protocol)
  Reliable connection-oriented protocol that allows a byte stream originating on one machine to be delivered without error on any other machine in the internet
  Fragments incoming byte stream into discrete messages
  Reassembles the received messages into the output stream
  Flow control to make sure a fast sender cannot swamp a slow receiver with more messages than it can handle

## Slide 79: The Transport Layer: UDP
UDP (User Datagram Protocol)
  Unreliable, connectionless protocol
  For applications that do not want TCP's sequencing or flow control and wish to provide their own (i.e. NFS)
  For applications in which prompt delivery is more important than accurate delivery, such as transmitting speech or video, DNS

## Slide 80: TCP/IP Model: in Details

## Slide 81: Protocols & networks in the TCP/IP
Protocols and networks in the TCP/IP model initially.

## Slide 82
Comparing OSI and TCP/IP Models

## Slide 83: 3 Concepts are Central to OSI Model
Services
  What the layer does, not how entities above it access it or how the layer works. It
Interfaces
  Tells the processes above it how to access it.
Protocols

## Slide 84: A Critique of the OSI Model & Protocols
Why OSI did not take over the world
  Bad timing
  Bad technology
  Bad implementations
  Bad politics

## Slide 85: Bad Timing
The apocalypse of the two elephants.

## Slide 86: Bad Technology
The choice of seven layers was more political than technical, and two of the layers (session and presentation) are nearly empty, whereas two other ones (data link and network) are overfull
Service definitions and protocols are extraordinarily complex and difficult to implement and inefficient in operation
Some functions, such as addressing, flow control, and error control, reappear again and again in each layer

## Slide 87: A Critique of the TCP/IP Reference Model
Problems
  Service, interface, and protocol not distinguished
  Not a general model
  Host-to-network “layer” not really a layer
  No mention of physical and data link layers
  Minor protocols deeply entrenched, hard to replace

## Slide 88: Hybrid Model
The hybrid reference model to be used in this book.

## Slide 89
1.5 Example Networks

## Slide 90: Example Networks
The Internet
The mobile phone network
Wireless LANs: 802.11
RFID/ Sensor networks

## Slide 91: The ARPANET
(a) Structure of the telephone system
(b) Baran’s proposed distributed switching system
Notes: Baran: packet-switching in military nets

## Slide 92: The Original ARPANET Design
Notes: 1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational

## Slide 93: Growth of the ARPANET
(a) December 1969 (b) July 1970 (c) March 1971
(d) April 1972. (e) September 1972.

## Slide 94: NSFNET
The NSFNET backbone in 1988.

## Slide 95: Internet Usage
Traditional applications (1970 – 1990)
  E-mail
  News
  Remote login
  File transfer
1990-
  WWW (World Wide Web) brought millions of new, nonacademic users to the net

## Slide 96: Architecture of the Internet
Overview of the Internet.

## Slide 97: The mobile phone network

## Slide 98: Wireless LANs
(a) Wireless networking with a base station.
(b) Ad hoc networking.

## Slide 99: Wireless LANs (2)
The range of a single radio may not cover the entire system.

## Slide 100: RFID / Sensor network

## Slide 101: Connection-Oriented Networks
X.25 (2.4K~64K)
  a computer first established a connection to the remote computer (Virtual Circuit)
  Data packet consists of a 3-byte header (VC#/seq#/ACK#) and up to 128 bytes of data.
Frame Relay (9.6K~2M)
  a connection-oriented network with no error control and no flow control
ATM (155M/622M)
  Transmit information in fixed-size packets called cells
  The cells are 53 bytes long, of which 5 bytes are header and 48 bytes are payload

## Slide 102
1.6 Network Standardization

## Slide 103: Network Standardization
Telecommunications World
  ITU (International Telecommunication Union)
  Main sectors
    Radio communications(ITU-R)
    Telecommunications Standardization(ITU-T)
      CCITT, Comité Consultatif International Télégraphique et Téléphonique (1956-1993)
    Development(ITU-D)
International Standards World
  ISO (International Standards Organization)
    ANSI (American National Standards Institute)
  IEEE (Institute of Electrical and Electronics Engineers)

## Slide 104: Internet Standards World
Internet协会（ISOC，Internet Society）
  推动、支持和促进Internet不断增长和发展的专业组织
  它把Internet作为全球研究通信的基础设施
体系结构委员会（IAB，Internet Architecture Board）
  技术监督和协调的机构。它由国际上来自不同专业的1 5个志愿者组成，其职能是负责Internet标准的最后编辑和技术审核
工程任务组（IETF，Internet Engineering Task Force）
  面向近期标准的组织，它分为9个领域（应用、寻径和寻址、安全等等）。IETF开发成为Internet标准的规范
研究任务组（IRTF，Internet Research Task Force）
  主要对长远的项目进行研究
IRTF和IETF隶属于IAB， IAB隶属于ISOC
  所有关于Internet的标准都以RFC(Request for Comment)文档出版
  Proposed Standard->Draft Standard->Internet Standard

## Slide 105: IEEE 802 Standards
The 802 working groups. The important ones are marked with *. The ones marked with  are hibernating. The one marked with † gave up.

## Slide 106: Metric Units
The principal metric prefixes
milli and micro both begin with the letter ''m', Normally, ''m'' is for milli and ''µ'' (the Greek letter mu) is for micro

## Slide 107: Highlights
purpose
subnet
classification
layer
protocol architecture
ISO OSI/rm
service primitive
connect 、connectless
famous architecture/Organization

## Slide 108: Homework
2, 3,9, 10, 11,16, 17, 18,30