## Slide 1: Chapter 2 The Physical Layer

## Slide 2: Highlights
Some concepts
The Theoretical Basis for Data Communication
Transmission medium
Wireless Transmission
Digital modulation and multiplexing
Message switch

## Slide 3: Simplified Data Communications Model

## Slide 4: Fundamental Concepts (1)
信道(Channel)：传送信息的媒体
数据率(Bit Rate)：数据传输速率 (bps)
波特(Baud)：码元传输速率
1 Baud = (log2V) bps，其中V是信号的电平级数
传播速度(Propagation Speed)：通信线路上，信号单位时间内传送的距离（米/秒）
带宽(Bandwidth)：信号占用的频率范围 (Hz)
信道容量(Channel Capacity)：信道的最大数据率
吞吐量(Throughput)：网络容量的度量，表示单位时间内网络可以传送的数据位数（bps）
误码率BER(Bit Error Rate)：信道传输可靠性指标
P= 传送错的位数 / 传送总位数

## Slide 5: Fundamental Concepts (2)
时延(Delay)：从向网络中发送数据块的第一比特开始，到最后一位数据被接收所经历的时间
时延的组成：传播时延、发送时延、处理时延、排队时延
  传播时延：信号通过传输介质的时间。
  发送时延：设备发送一个数据块所需要的时间（数据块长度/信道带宽)
  处理时延：交换机/路由器检查数据、选路的时间
  排队时延：在交换机/路由器中排队等待的时间

## Slide 6: Sources of Delay (1)
1. Nodal processing delay
  check bit errors
  determine output link
2. Queueing dealy:
  time waiting at output link for transmission
  depends on congestion level of router

## Slide 7: Sources of Delay (2)
3. Transmission delay:
  R=link bandwidth (bps)
  L=packet length (bits)
  time to send bits into link = L/R
4. Propagation delay:
  d = length of physical link
  s = propagation speed in medium
  propagation delay = d/s

## Slide 8: Simplex, Half-duplex, Full-duplex
Simplex
  Transmission occurs in only one direction
  eg. FM Radio broadcasting
Half-duplex
  Transmission can be made in both direction, but at one time only one direction is available
  eg. talkie and walkie （对讲机）
Full-duplex
  Transmission can be made in both directions simultaneously
  eg. Phone conversation
Notes: 传输模式

## Slide 9: Parallel transmission vs. Serial transmission

## Slide 10: Asynchronous Transmission vs. Synchronous Transmission
Notes: 异步传输：
  独立时钟，无须同步
  以字符为单位进行传输
  发送两个字符之间的间隔是任意的
  接收方依靠字符中的起始位来同步
同步传输：以时钟来对传输进行同步
以数据块（帧或分组）为单位传输

## Slide 11: 同步串行传输和异步串行传输
同步串行传输
  以时钟信号线对传输的数据线上的信号进行比特同步
  以数据块（帧或分组）为单位传输
异步串行传输
  独立时钟，无须同步
  以字符为单位进行传输
  发送两个字符之间的间隔是任意的
  接收方依靠字符中的起始位和停止位来同步

## Slide 12: 2.1 The Theoretical Basis for Data Communication

## Slide 13: The Theoretical Basis for Data Communication
Fourier Analysis
Bandwidth-Limited Signals
Maximum Data Rate of a Channel

## Slide 14: Fourier Analysis

## Slide 15: Bandwidth-Limited Signals
(a) A binary signal (‘b’) and its root-mean-square Fourier amplitudes.
(b) – (e) Successive approximations to the original signal.

## Slide 16: Bandwidth-Limited Signals (2)
The range of frequencies transmitted without being strongly attenuated is called the bandwidth.
For example, a telephone wire may have a bandwidth of 1 MHz for short distances

## Slide 17: Bandwidth-Limited Signals (3)
T=8/b, first harmonic f=b/8
voice-grade line:
Max harmonics=3000/f=24000/b
When data rates ≥38.4 kbps, there is no hope at all for binary signals, even if the transmission facility is completely noiseless.
Notes: T=1000/b*8
Hz=b/8
3000hz

## Slide 18: Bandwidth
  No transmission facility can transmit signal without losing some power
  All transmission facilities diminish different Fourier components by different amounts
  Range of frequencies transmitted without being strongly (0.5) attenuated is called bandwidth
    Telephone wire’s bandwidth: 1 MHz
    UTP 5: 100MHz
  bandwidth is a physical property of the transmission medium, depends on
    construction
    thickness
    length
    bandwidth (Hz, bps)

## Slide 19: Maximum Data Rate of a Channel
Nyquist's theorem (1924)
  If a signal has been run through a low-pass filter of bandwidth H, the signal can be completely reconstructed by making 2H samples per second
  C=2Hlog2V
Shannon’s Theorem (1948)
Example: Voice phone line 300Hz-3300Hz, S/N dB=30dB

## Slide 20: Maximum Data Rate of a Channel（2）
Shannon’s Theorem (1948)
Example: ADSL 1MHz, S/N dB=40dB

## Slide 21: 2.2 Guided Transmission Media

## Slide 22: Guided Transmission Media
Magnetic Media
Twisted Pair
Coaxial Cable
Power line
Fiber Optics

## Slide 23: Magnetic Media
Bandwidth (bps)
  A tape can hold 800 GB,
  A box can hold 1000 tapes: 800 TB,
  24小时快递,
  bandwidth=800T x 8bits/86400s sec=70 Gbps
Cost
  tape cost $4000 per box per usage
  $1000 for shipping
  shipping 1 GB for under 0.5 cents

## Slide 24: Twisted Pair
Category 3 UTP
Category 5 UTP
Most common transmission media, Can be used for
transmitting either analog or digital signals
Two insulated copper wires, about 1 mm thick, the
wires are twisted together in a helical form(螺旋状)
Two parallel wires constitute a fine antenna. When
the wires are twisted, the waves from 2 wires cancel
out, so the wire radiates less effectively(串扰：自身信
号对环境影响)
The bandwidth depends on the thickness of the wire and the distance traveled, several megabits/sec can be achieved for a few kilometers

## Slide 25: Twisted Pair (2)
Category 3 UTP
Category 5 UTP
UTP & STP
Bandwidth
  Category 3 UTP: 16MHz
  Category 5 UTP: 100MHz
  Category 6 UTP: 250MHz
  Category 7 UTP: 600MHz

## Slide 26: Coaxial Cable
It can span longer distances at higher speeds
Two kinds of coaxial cable are widely used
  50-ohm cable, is commonly used when it is intended
  for digital transmission
  75-ohm cable, is commonly used for analog
  transmission and cable television
High bandwidth(1GHz)
Excellent noise immunity

## Slide 27: Power line
both inside the home as a LAN and outside the home for broadband Internet access
designed to distribute power signals

## Slide 28: Fiber Cables
From 1981 to 2009
CPU (4.77M to 3G Hz)
  A gain of a factor of 16 per decade
  Physical limits: speed of light, heat dissipation
Data communication (45M to 100G bps)
  A gain of a factor of 16 per decade
  Error rate: 10-5 to almost 0
(a) Side view of a single fiber
(b) End view of a sheath with three fibers

## Slide 29: Comparison of Fiber and Copper ware
High bandwidth
Lightweight
Security

## Slide 30: 2.3 Wireless Transmission

## Slide 31: The Electromagnetic Spectrum
Electromagnetic spectrum and its uses for communication

## Slide 32: Transmission Frequency Band
Using narrow frequency band
  Most transmission use narrow frequency band to get the best reception
Spread Spectrum (bluetooth, wlan, cdma)
  FHSS: Frequency hopping spread spectrum
  Hedy Lamarr (1913-2000)
  DSSS: Direct sequence spread spectrum
  UWB (Ultra-WideBand) communication.
  UWB sends a series of rapid pulses, varying their positions to communicate information.

## Slide 33: Radio Transmission (VLF,LF,MF,HF)
(a) In the VLF, LF, and MF bands, radio waves follow the curvature of the earth (1000km)
(b) In the HF band, they bounce off the ionosphere at a height of 100~500 km

## Slide 34: Microwave Transmission
  Microwave(100M~10GHz)
  Before fiber optic, microwaves formed the heart of the long-distance telephone transmission system
  waves travel in nearly straight lines, the transmitting & receiving antennas must be accurately aligned
  Distance between repeaters: 80km
  Multipath fading is often a serious problem (weather and frequency dependent)
  (At about 4GHz, absorbed by rain)

## Slide 35: Politics of Electromagnetic Spectrum
National governments allocate spectrum
  Worldwide:ITU-R; USA: FCC
ISM (Industrial, Scientific, Medical) bands
  some frequency bands for unlicensed usage
  FCC mandates that all devices in ISM bands use spread spectrum techniques to minimize interference between uncoordinated devices
  Power is under 1 watt
  （限制频率范围，调制技术，信号强度）
ISM bands in USA

## Slide 36: Infrared Transmission
widely used for short-range communication
relatively directional, cheap
do not pass through solid objects
no government license is needed to operate
an infrared system

## Slide 37: Lightwave Transmission
(Unguided optical signaling)
  Aiming a 1-mm-wide laser beam at a small target 500m away, ...
  Laser beams cannot penetrate rain or thick fog
Convection currents interfere with laser communication systems

## Slide 38: 2.4 Communication Satellites

## Slide 39: Communication Satellites
Act as a big microwave repeater in the sky
  Contains multiple antennas and multiple transponders
Transponder
  listen to some portion of the spectrum
  amplifies the incoming signals
  rebroadcasts it at another frequency (downward beams)
Downward beams
  Broad: a substantial fraction of the earth’s surface
  Narrow: spot beams cover an area hundreds of kms in diameter (bent pipe)
Station keeping
  Lifetime: about 10 years
Notes: 波束

## Slide 40: Communication Satellites and Some of Their Properties
altitude above the earth, round-trip delay time and number of satellites needed for global coverage

## Slide 41: The Principal Satellite Bands
A modern satellite has around 40 transponders, each with an 80-MHz bandwidth

## Slide 42: GEO: VSATs Using a Hub
Problem
  Micro-station do not have enough power to communicate directly with one another via the satellite

## Slide 43: LEO: Iridium
LEO
  The ground stations do not need much power
  Round-trip delay is only a few ms
Iridium
  Altitude: 750km
  6 satellite necklaces, 11x6=66 satellites
  Each satellite has a max of 48 cells (spot beams)
  1628 moving cells cover the earth
  Communication between distant customers takes place in space
实施情况
  90年策划，97年发射，98年运营，99年破产
  受到移动电话网的冲击

## Slide 44: Iridium Cells
(a) The Iridium satellites form six necklaces around the earth
(b) 1628 moving cells cover the earth

## Slide 45: LEO: Globalstar
48 LEOs satellites
Relaying on the ground
  puts much of the complexity on the ground, ease to manage
  lower-powered telephones can be used (a few milliwatts)

## Slide 46: Iridium & Globalstar
(a) Relaying in space.
(b) Relaying on the ground.

## Slide 47: 2.5 Digital modulation and multiplexing

## Slide 48: Baseband transmission
bandwidth efficiency, clock recovery, and DC balance.
NRZ
NRZI
Manchester
AMI

## Slide 49: Baseband transmission

## Slide 50: Baseband transmission
bandwidth efficiency
  NRZ need a bandwidth of at least B/2 Hz when the bit rate is B bits/sec (C=2Hlog2V)
  bit rate=baud rate * the number of bits per symbol
  the number of signal levels does not need to be a power of two
clock recovery
  Manchester / NRZI
  4B/5B never be a run of more than three consecutive 0s
Notes: 波束

## Slide 51: balanced signals
Use two voltage levels to represent a logical 1
8B/10B
The 8 bits are split into a group of 5 bits, which is mapped to 6 bits, and a group of 3 bits, which is mapped to 4 bits.

## Slide 52: Passband Transmission
(a) A binary signal
(b) Amplitude modulation
(c) Frequency modulation
(d) Phase modulation

## Slide 53: QPSK & QAM
(a) QPSK.
(b) QAM-16.
(c) QAM-64.
Notes: QPSK 正交相移键控

## Slide 54: Frequency Division Multiplexing
(a) The original bandwidths.
(b) The bandwidths raised in frequency.
(b) The multiplexed channel.

## Slide 55: Time Division Multiplexing

## Slide 56: CDMA – Code Division Multiple Access

## Slide 57: Wavelength Division Multiplexing
WDM (Wavelength Division Multiplexing).
DWDM (Dense WDM).
the bandwidth of a single fiber band is about 25,000 GHz

## Slide 58: 2.6 The Public Switched Telephone Network

## Slide 59: Public Switched Telephone System (PSTN)
The Local Loop: Modems, ADSL and Wireless
Trunks and Multiplexing
Switching

## Slide 60: Structure of the Telephone System
(a) Fully-interconnected network.
(b) Centralized switch.
(c) Two-level hierarchy.

## Slide 61: Structure of the Telephone System (2)
A typical circuit route for a medium-distance call

## Slide 62: Components of Telephone System
Local loops
  Analog twisted pairs going to houses and businesses
Trunks
  Digital fiber optics connecting the switching offices
Switching offices
  Where calls are moved from one trunk to another

## Slide 63: The Local Loop Modems, ADSL, and Fiber

## Slide 64: Problems
Transmission lines suffer from three major problems
  Attenuation（衰减）
  delay distortion（延迟畸变）
  Noise
(前两项的变化程度与频率相关）
Modem & ADSL

## Slide 65: Modems
The use of both analog and digital transmissions for a computer to computer call. Conversion is done by the modems and codecs.
CODEC:
8000 samples per second
1 sample = 8 bits (非线性编码)

## Slide 66: Modems
Modems use a combination of modulation techniques to transmit multiple bits per baud
（multiple amplitudes and multiple phase shifts）
  QPSK: Quadrature Phase Shift Keying-相移键控
  QAM : Quadrature Amplitude Modulation-正交幅度调制
Modems sample 2400 times/sec and focus on getting more bits per sample
  V.32: 2400 baud * (5-1) bits = 9.6Kbps
  V.32bis: 2400 baud * (7-1) bits = 14.4Kbps
  V.34: 2400 baud * 12 bits = 28.8Kbps
  V.34bis: 2400 baud * 14 bits = 33.6Kbps
V.90(56kbps)

## Slide 67: V.32 & V.32bis
(a) V.32 for 9600 bps.
(b) V32 bis for 14,400 bps.
(a)
(b)

## Slide 68: DSL: Digital Subscriber Lines
Bandwidth versus distanced over category 3 UTP for DSL.

## Slide 69: ADSL: Discrete Multitone Modulation
Divide 1.1 MHz into 256 channels of 4312.5 Hz
Channel 0 for POTS
1–5 not used, to keep voice signal and data signals from interfering with each other
250 channels
  Upstream control (1)
  Downstream control (1)
  User data (248)

## Slide 70: ADSL Modulation Scheme
Within each channel, a modulation scheme similar to V.34 is used
  Sampling rate is 4000 baud
  The line quality in each channel is monitored and data rate adjusted continuously
  The actual data are sent with QAM modulation, with up to 15 bits/baud
G.dmt
  8Mbps, 1Mbps
  12Mbps, 1Mbps ADSL2；24Mbps ADSL2+
  Standard service: 1 Mbps, 256 kbps
  Improved service: 4 Mbps, 1 Mbps
  Premium service: 8 Mbps, 2 Mbps
Notes: 标准改进和高级

## Slide 71: A typical ADSL equipment configuration
Notes: Digital Subscriber Line Access Multiplexer (DSLAM)

## Slide 72: FttH

## Slide 73: Trunks and Multiplexing

## Slide 74: Time Division Multiplexing
The T1 carrier (1.544 Mbps).
E1 2.048Mbps

## Slide 75: Time Division Multiplexing (2)
Multiplexing T1 streams into higher carriers.

## Slide 76: Switching

## Slide 77: Circuit Switching
(a) Circuit switching.
(b) Packet switching.

## Slide 78: Packet switching
A node in a packet switching network
incoming links
outgoing links
Node
Memory

## Slide 79: Message Switching
(a) Circuit switching (b) Message switching (c) Packet switching

## Slide 80: Circuit switched and packet-switched networks
.

## Slide 81: 2.7 Physical Interface

## Slide 82: 物理层接口特性
机械特性 指明接口所用接线器的形状和尺寸、引线数目和排列、固定和锁定装置等等
电气特性 指明在接口电缆的各条线上出现的电压的范围
功能特性 指明某条线上出现的某一电平的电压表示何种意义
过程特性 指明对于不同功能的各种可能事件的出现顺序

## Slide 83
EIA RS-232 （ITU-T V.24）
Physical Interface
First issued by EIA in 1969
EIA-232-C EIA-232-D EIA-232-E
Interface standard between DTE and DCE
  DTE Data Terminal Equipment
  DCE Data Circuit Equipment

## Slide 84
Mechanical ：25-pin
Electrical：<-3V “1”， >3“0”
data rate 20Kbps
cable <15 m
Functional：pin definition
Procedure： protocol
RS-232

## Slide 85
RS-232 ：signal
DTE: data terminal equipment
DCE: data communications equipment
TD: Transmitted data
RD: Received data
RTS: Request to send
CTS: Clear to send
DSR: data set ready
CD: Data Carrier detection
DTR: Data Terminal Ready

## Slide 86
Virtual MOEM

## Slide 87
DTE
DTE
2
2
3 RD
3
7 GND
7
TD
Virtual MOEM(2)