## Slide 1
3 The Data Link Layer

## Slide 2: Highlights
Framing
Error-Control
  Error-correction
  Error-detection
ARQ (Automatic Repeat reQuest)
Flow control
  Stop-Wait
  Slide Window
Performance
ADSL、HDLC、SLIP和PPP

## Slide 3
3.1 Data Link Layer Design Issues

## Slide 4: Data Link Layer Design Issues
Goals
  Study the algorithms for achieving reliable, efficient communication between two adjacent machines
  Adjacent: two machines are connected by a communication channel that acts conceptually like a wire, bits are delivered in exactly the same order in which they are sent.
Data Link Layer Design Issues
  Services Provided to the Network Layer
  Framing
  Error Control
  Flow Control

## Slide 5
Services Provided to the Network Layer

## Slide 6: Functions of the Data Link Layer
Provide service interface to the network layer
Dealing with transmission errors
Regulating data flow
  Slow receivers not swamped by fast senders
Notes: 调节： Regulating

## Slide 7: Functions of the Data Link Layer (2)
Relationship between packets and frames.

## Slide 8: Services Provided to Network Layer
(a) Virtual communication.
(b) Actual communication.

## Slide 9: Services Provided to Network Layer(2)
Unacknowledged connectionless service.
Most LANs use unacknowledged connectionless service
Acknowledged connectionless service.
This service is useful over unreliable channels, such as wireless systems
Acknowledged connection-oriented service
10 frames, of which 2 are lost on average. It would then take a very long time for the packet to get through.
  Connection establishment
  Timer
  Sequence number
Notes: 0.8^10=0.1
1/0.1=10

## Slide 10
Framing

## Slide 11: Framing
A sequence of bits is sent from node A to node B over a point-to-point link. Node B must recognize exactly what set of bits constitutes a frame, that is, it must determine where the frame begins and ends.

## Slide 12: Character Count
A character stream.
(a) Without errors. (b) With one error.
Character count(字符计数):
Uses a field in the header to specify the number of characters in the frame (DEC:DDCMP)

## Slide 13: Byte Stuffing
(a) A frame delimited by flag bytes.
(b) Four examples of byte sequences before and after stuffing.
Flag bytes with byte stuffing (字符添充):Having each frame start and end with special bytes (IBM:BISYNC)

## Slide 14: Bit Stuffing
(a) The original data.
(b) The data as they appear on the line.
(c) The data as they are stored in receiver’s memory after destuffing.
Starting and ending flags, with bit stuffing (比特添充):Each frame begins and ends with a special bit pattern, 01111110 . Whenever the sender's data link layer encounters five consecutive 1s in the data, it automatically stuffs a 0 bit into the outgoing bit stream (Example: HDLC)
Notes: 10101111110 111110011 10101010 111110111 01010101 0111 1110 11101110

## Slide 15: Example with Possible Errors (Bit Stuffing)

## Slide 16: 比特填充
从信道上收到比特序列： 1101 0111 1110 0111 1110 1101 1011 1110 0010 1100 0101 1111 0101 1001 1111 1001，该比特序列中包含一个完整的帧，用十六进制写出该帧的内容（不包含帧的首尾标志）。
HDLC使用比特填充法成帧，帧定界符为01111110，在帧的内容中若出现连续的5个1，则立即插入1个0，应该去掉加入的0,完整的帧内容：
Notes: 1101 1011 1110 0101 1000 1011 1111 0110
D B E 5 8 B F 6

## Slide 17: Physical Layer Coding Violations
Physical layer coding violations:物理层编码违例法 (IEEE:802.3)

## Slide 18
Error Control & Flow Control

## Slide 19: Error Control
Make sure all frames are eventually delivered to the network layer at the destination and in the proper order
  Provide the sender with some feedback about what is happening at the other end of the line
  Hardware troubles may cause a frame to vanish completely
    If either the frame or the ACK is lost, the timer will go off, alerting the sender to a potential problem
    Managing the timers and sequence numbers so as to ensure that each frame is ultimately passed to the network layer at the destination exactly once, no more and no less

## Slide 20: Flow Control
What to do with a sender that wants to transmit frames faster than the receiver can accept them
Two approaches are commonly used
  Feedback-based flow control, the receiver sends back information to the sender giving it permission to send more data or at least telling the sender how the receiver is doing
  Rate-based flow control, the protocol has a built-in mechanism that limits the rate at which senders may transmit data, without using feedback from the receiver.

## Slide 21: Flow Control

## Slide 22
3.2 Error Detection and Correction

## Slide 23: Error Control
Classification of Errors
  Lost frames: a frame failed to arrive to the other side
    Owing to noise burst or dropped from a queue
  Damaged frames: some bits are in error
Error detection
  Parity check: able to detect single bit errors
  Cyclic Redundancy Check (CRC): detecting some burst errors
  Automatic Repeat reQuest (ARQ)
Error correction
  Forward Error Correction (FEC)

## Slide 24: Single-bit Error & Burst Error
Single-bit error, only one bit has changed
A burst error means that 2 or more bits have changed.

## Slide 25
Error Correcting Code

## Slide 26: Hamming Distance
Hamming distance: The number of bit positions in which two codewords differ
  (10001001 and 10110001, Hamming distance = 3)
To detect d errors, need a distance d+1 code
To correct d errors, need a distance 2d+1 code

## Slide 27: Example of an Error-Correcting Code
  Consider a code with only four valid codewords:
0000000000, 0000011111
1111100000, 1111111111
  This code has a distance 5, which means that it can correct 2 errors.
    If the codeword 0000000111 arrives, the receiver knows that the original must have been 0000011111
    If a triple error changes 0000000000 into 0000000111, the error will not be corrected properly

## Slide 28: Hamming code
The number of check bits needed to correct single errors：
  m+r+1≤ 2r m: message bits, r:check bits
m message bits and r check bits, 2m legal messages, n = m + r
Each legal message has n illegal codewords at a distance 1 from it
(n + 1)2m ≤ 2n
(m + r + 1) ≤ 2r.
Example: m=7,r≥4

## Slide 29: Hamming code
The bits of the codeword are numbered, start with 1 at left end, bit 2 to its immediate right, and so on.
The bits that are powers of 2 (1, 2, 4, 8, 16, etc.) are check bits. Each check bit forces the parity of some collection of bits, including itself, to be even (or odd).
The rest (3, 5, 6, 7, 9, etc.) are filled up with the m data bits
even parity ‘H’ 100,1000
3=1+2， 5=1+4， 6=2+4， 7=1+2+4 , 9=1+8,
10=2+8, 11=1+2+8 so bit1 (3,5,7,9,11)
Bit number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Bit value | ？ （0） | ？ | 1 | ？ | 0 | 0 | 1 | ？ | 0 | 0 | 0

## Slide 30: Error Crrection

## Slide 31: Hamming code: Correct burst errors
Use of a Hamming code to correct burst errors.

## Slide 32: Other error-correcting codes
Binary convolutional codes.
Reed-Solomon codes.
Low-Density Parity Check codes.

## Slide 33
Error Detecting Code

## Slide 34: Detection code
1、Parity
2、Checksums
3、Cyclic Redundancy Checks (CRCs)

## Slide 35: Error Correcting & Detecting
On channels that are reliable, such as fiber, it is cheaper to use an error detecting code and just retransmit the occasional block found to be faulty
On channels such as wireless links that make many errors, it is better to add enough redundancy to each block for the receiver to be able to figure out what the original block was
Example (single-bit error)
  Bit Error Rate BER=10-6, 1Block=1000bits, Data=1M bits
  The overhead
    Error detection + retransmission: 2001 bits
    Hamming code : 10,000 bits
(m + r + 1) ≤ 2r

## Slide 36: Error Detecting Codes

## Slide 37: Odd & Even Parity
Odd & Even parity

## Slide 38: Odd & Even Parity
Coding
  Each block to be sent is regarded as a matrix
  A parity bit is computed separately for each column and affixed to the matrix as the last row
  The matrix is then transmitted one row at a time.
Performance
  Can detect a single burst of length n
  A burst of length n + 1 will pass undetected if the first bit is inverted, the last bit is inverted, and all the other bits are correct
10010001
01010011
10100001
01010110
11001100
11101101
10001000
10011110
n

## Slide 39: Checksums
Word Cksum(Word *Buf, Word Num_Words)
{
Dword Sum;
for ( Sum=0; Num_Words>0; Num_Words--)
Sum+=*Buf++;
Sum = ( Sum >> 16 ) + ( Sum & 0xffff );
Sum += Sum >> 16;
return ~Sum;
}

## Slide 40: Polynomial Code
Also known as CRC (Cyclic Redundancy Check)
Treating bit strings as representations of polynomials with coefficients of 0 and 1
  A k-bit frame is regarded as the coefficient list for a polynomial with k terms, ranging from xk-1 to x0: 110001=> x5 + x4 + x0
Polynomial arithmetic is done modulo 2, addition and subtraction are identical to XOR
The algorithm for computing the checksum:
  The degree of generator polynomial G(x), is r
  Append r zero bits to the low-order end of the frame（xr M(x) ）
  Divide the bit string corresponding to G(x), using modulo 2 division
  Subtract the remainder from the bit string using modulo 2 subtraction （T(x)）

## Slide 41
Calculation of the
polynomial code checksum.

## Slide 42: CRC code

## Slide 43: The Power of CRC (1)
Imagine that a transmission error occurs, so that instead of the bit string for T(x) arriving, T(x) + E(x) arrives.
Upon receiving the checksummed frame, the receiver computes [T(x) + E(x)]/G(x). T(x)/G(x) is 0, so the result is E(x)/G(x). Those errors that happen to correspond to polynomials containing G(x) as a factor will slip by; all other errors will be caught.

## Slide 44: The Power of CRC (2)
A polynomial code with r check bits will detect all burst errors of length ≤ r
By making x+1 a factor of G(x), we can catch all errors consisting of an odd number of inverted bits
Burst length is r + 1 ，an incorrect frame being accepted as valid is ½r – 1.
The probability of a bad frame(Burst length is longer than r + 1 ) getting through unnoticed is ½r, assuming that all bit patterns are equally likely

## Slide 45: Generator Polynomial
Certain polynomials have become international standards
CRC-16
  x16+x15+x2+1
CRC-CCITT (HDLC)
  x16+x12+x5+1
CRC-32 (IEEE802)
  x32+x26+x23+x22+x16+x12+x11+x10+x8+x7+x5+x4+x2+x1+1

## Slide 46: The Calculation of CRC
Hardware
  A simple shift register circuit can be constructed to compute and verify the checksums
Software
static u16 fcstab[256] = {
0x0000, 0x1189, 0x2312, 0x329b, 0x4624, 0x57ad, 0x6536,
0x74bf, 0x8c48, 0x9dc1, 0xaf5a, 0xbed3, 0xca6c, 0xdbe5,
……
0xd49d, 0xc514, 0xb1ab, 0xa022, 0x92b9, 0x8330, 0x7bc7,
0x6a4e, 0x58d5, 0x495c, 0x3de3, 0x2c6a, 0x1ef1, 0x0f78
};
u16 fcs16(u16 fcs, unsigned char *cp, int len)
{
while (len--)
fcs = (fcs >> 8) ^ fcstab[(fcs ^ *cp++) & 0xff];
return (fcs);
}
Notes: 链路层第一次作业

## Slide 47
3.3 Elementary Data Link Protocols

## Slide 48: Elementary Data Link Protocols
An Unrestricted Simplex Protocol
A Simplex Stop-and-Wait Protocol
A Simplex Protocol for a Noisy Channel

## Slide 49
Protocol Definitions

## Slide 50: Elementary Data Link Protocols
Some of the assumptions
  Physical layer, data link layer, and network layer are independent processes
  Machine A wants to send a long stream of data to machine B, using a reliable, connection-oriented service
  Machines do not crash
  There exist suitable library procedures to_physical_layer to send a frame and from_physical_layer to receive a frame

## Slide 51: Protocol Definitions
Some definitions needed in the protocols to follow. These are located in the file protocol.h.

## Slide 53
Protocol 1: Utopia

## Slide 55
Protocol 2:
Stop-and-Wait Protocol for a Error-free Channel

## Slide 57
Protocol 3:
A Simplex Protocol for a Noisy Channel

## Slide 58: Stop-And-Wait
Time
A
B
DATA
ACK
DATA
ACK
(a) Normal
A
B
DATA
DATA
ACK
(c) Data Lost
tout
Lost
！
A
B
DATA
ACK
DATA
ACK
(d) ACK Lost
tout
Lost
！
A
B
DATA
NAK
DATA
ACK
(b) Data Error
Err

## Slide 59: Problems
Case 1: Protocol failed on receiver
  The network layer on A gives packet 1 to its data link layer. The packet is correctly received at B and passed to the network layer on B. B sends an ACK frame back to A.
  The ACK gets lost completely
  The data link layer on A eventually times out. Not having received an acknowledgement, it sends the frame containing packet 1 again
  The duplicate frame also arrives B and is passed to the network layer
Case 2: Protocol failed on Sender
  A delayed ACK

## Slide 60: Sequence Number
Distinguish a frame that it is seeing for the first time from a retransmission
  Put a sequence number in the header of each frame
What is the minimum number of bits needed for the sequence number?
  链路层：1比特，编号空间大小为2
  传输层：1比特编号空间太小，需要较大的编号空间使得在编号回卷时，保证同编号的旧帧不可能被缓冲在网络中，如：TFTP

## Slide 61: Sender
  从网络层获取一个分组放入buffer
  发送buffer中的数据，新启动定时器
label1:
  wait_for_event()
  switch (event) {
  case 收到了坏帧(校验和错):
  重发缓冲在buffer里的数据，重新启动定时器
  case 定时器超时：
  重发缓冲在buffer里的数据，新启动定时器
  case 收到校验和正确的帧：
  if（ack序号正确） {
  关闭旧定时器
  从网络层获取下一个分组放入buffer
  发送buffer中的数据，新启动定时器
  } else
  重发缓冲在buffer里的数据，重新启动定时器
  }
  goto label1

## Slide 62: Sender
  从网络层获取一个分组放入buffer
  发送buffer中的数据，新启动定时器
label1:
  wait_for_event()
  switch (event) {
  case 收到了坏帧(校验和错):
  重发缓冲在buffer里的数据，重新启动定时器
  case 定时器超时：
  重发缓冲在buffer里的数据，新启动定时器
  case 收到校验和正确的帧：
  if（ack序号正确） {
  关闭旧定时器
  从网络层获取下一个分组放入buffer
  发送buffer中的数据，新启动定时器
  } else
  重发缓冲在buffer里的数据，重新启动定时器
  }
  goto label1

## Slide 63: Sender
  从网络层获取一个分组放入buffer
  发送buffer中的数据，启动定时器
while(true) {
  wait_for_event()
  if (收到校验和正确的帧) {
  if（ack序号正确） {
  关闭旧定时器
  从网络层获取下一个分组放入buffer
  }
  }
  发送buffer中的数据，启动定时器
}

## Slide 64: Sender
  从网络层获取一个分组放入buffer
while(true) {
  发送buffer中的数据，启动定时器
  wait_for_event()
  if (收到校验和正确的帧) {
  if（ack序号正确） {
  关闭旧定时器
  从网络层获取下一个分组放入buffer
  }
  }
}

## Slide 65: Sender
  从网络层获取一个分组放入buffer
  next_frame_to_send = 0;
while(true) {
  发送buffer中的数据，启动定时器
  帧序号填写为next_frame_to_send
  wait_for_event()
  if (收到校验和正确的帧) {
  if（ack序号正确） {
  关闭旧定时器
  从网络层获取下一个分组放入buffer
  inc(next_frame_to_send)
  }
  }
}
（next_frame_to_send 记录目前缓冲在buffer中的数据的编号。
buffer中装入下一个数据， next_frame_to_send 加1）

## Slide 66: Sender

## Slide 67
frame_expected=0
while(true) {
  wait_for_event()
  switch(event) {
  case 坏帧：
  do_nothing
  case 收到校验和正确的数据帧:
  if（序号==frame_expected） {
  向网络层上交分组
  回ACK（序号为frame_expected)
  inc(frame_expected)
  } else {
  回ACK（序号为frame_expected-1)
  }
  }
}
Receiver

## Slide 68
frame_expected=0
while(true) {
  wait_for_event()
  if (event==收到校验和正确的数据帧) {
  if（序号==frame_expected） {
  向网络层上交分组
  inc(frame_expected)
  回ACK（序号为frame_expected-1)
  } else {
  回ACK（序号为frame_expected-1)
  }
  }
}
Receiver

## Slide 69
frame_expected=0
while(true) {
  wait_for_event()
  if (event==收到校验和正确的数据帧) {
  if（序号==frame_expected） {
  向网络层上交分组
  inc(frame_expected)
  }
  回ACK（序号为frame_expected-1)
  }
}
Receiver

## Slide 70: Receiver
A positive acknowledgement with retransmission protocol.

## Slide 71: Timer
Timeout
  If the timeout interval is set too short, the sender will transmit unnecessary frames. While these extra frames will not affect the correctness of the protocol, they will hurt performance

## Slide 72
3.4 Sliding Window Protocols

## Slide 73: Piggybacking
For full-duplex data transmission:
  Use two separate communication channels and use each one for simplex data traffic
  Use the same circuit for data in both directions
Piggybacking
  When a data frame arrives, instead of immediately sending a separate control frame, the receiver restrains itself and waits until the network layer passes it the next packet
  ACK is attached to the outgoing data frame (using the ack field in the frame header).

## Slide 74: Sending window & Receiving window
Sending window
  At any instant of time, the sender maintains a set of sequence numbers corresponding to frames it is permitted to send. These frames are said to fall within the sending window
Receiving window
  Receiver also maintains a receiving window corresponding to the set of frames it is permitted to accept

## Slide 75: Sliding Window Protocols
A One-Bit Sliding Window Protocol
A Protocol Using Go Back N
A Protocol Using Selective Repeat

## Slide 76
One-Bit Sliding Window Protocol

## Slide 77: Sliding Window of Size 1
A sliding window of size 1, with a 3-bit sequence number.
(a) Initially.
(b) After the first frame has been sent.
(c) After the first frame has been received.
(d) After the first acknowledgement has been received.

## Slide 78: One-Bit Sliding Window Protocol (1)

## Slide 79: One-Bit Sliding Window Protocol (2)

## Slide 80: Two Scenarios for Protocol 4
Two scenarios for protocol 4.
The notation is (seq, ack, packet)
An asterisk indicates where a network layer accepts a packet
(a) Normal case. (b) Abnormal case.

## Slide 81: Problem
Consider a 50-kbps satellite channel with a 500-msec round-trip propagation delay, send 1000-bit frames
  t=0: sender starts sending
  t=20 msec: the frame has been completely sent
  t=270 msec: frame fully arrived at the receiver
  t=520 msec: ACK arrived back at the sender, under the best of circumstances (no waiting in the receiver and a short acknowledgement frame).
Conclusion
  Sender was blocked during 500/520 or 96% of the time. only 4% of the available bandwidth was used

## Slide 82: Line Utilization
Channel capacity is B bits/sec
Frame size l bits
propagation time R sec
Line Utilization
  (l/B)/(l/B+2R)=l/(l+2BR)=1/(1+2BR/l)
  If l < 2BR, the efficiency will be less than 50 percent

## Slide 83
Protocol Using Go Back N

## Slide 84: Pipelining & Error Recovery
Pipelining and error recovery. Effect on an error when
(a) Receiver’s window size is 1.
(b) Receiver’s window size is large.

## Slide 85: Go Back N（GBN）
Based on sliding window
Use window to control number of outstanding frames
If Receiver detects error, discard that frame and all future frames until error frame received correctly
Transmitter must go back and retransmit that frame and all subsequent frames

## Slide 86: Damaged Frame
If Data Frame is Damaged
  Receiver detects error in frame i
  Receiver discard that frame i and all subsequent
  When timeout transmitter retransmits frame i and all subsequent
If ACK Frame is Damaged
  Receiver gets frame i and send acknowledgement ACK (i) which is lost
  Ack are cumulative, so next ACK(i+n) may arrive before transmitter times out on frame i
  If transmitter times out, retransmits frame i and all subsequent

## Slide 87: About ACK
B
A
0
1
2
ACK0
ACK2
ACK1
B
A
0
1
2
ACK2

## Slide 88: Maximum of Sending Window Size
The sender sends frames 0 through 7.
A piggybacked acknowledgement for frame 7 eventually comes back to the sender.
The sender sends another eight frames, again with sequence numbers 0 through 7.
Now another piggybacked acknowledgement for frame 7 comes in
原则
  当发送方发送完发送窗口内所有帧，在未收到ACK之前，接收方正确接收到所有发送来的帧，接收窗口向前推移，此时，必须保证发送窗口与接收窗口在序号上不能重叠

## Slide 93: Protocol 5:Go-Back-N Protocol
发送窗口最大值7

## Slide 94: Protocol5改进和效率
设置ACK定时器
  发送数据并非一个源源不断的分组流，无法及时搭载ACK 时，发送ACK帧
  用于回送ACK的定时器start_ack_timer与stop_ack_timer
  与数据重传所用定时器start_timer与stop_timer的区别
  ACK定时器时限的设计
协议参数与线路利用率
  超时定时器时限的设计（考虑线路往返时间延迟，ACK定时器时限，对方物理层发送排队时延）
  滑动窗口即MAX_SEQ大小

## Slide 95: Timer Queue in Software
Simulation of multiple timers in software.

## Slide 96
Using Selective Repeat

## Slide 97: Selective Repeat
Also called Selective Reject（SR）
Only Rejected frames are retransmitted
Subsequent frames are accepted by the receiver and buffered
Minimizes retransmission
Receiver must maintain large enough buffer
More complex

## Slide 98: Window Size of Selective Repeat
(a) Initial situation with a window size seven.
(b) After seven frames sent and received, but not acknowledged.
(c) Initial situation with a window size of four.
(d) After four frames sent and received, but not acknowledged

## Slide 99: Sequence Number, Buffers
The maximum window size should be at most half the range of the sequence numbers
How many buffers must the receiver have?
  The number of buffers needed is equal to the window size, not to the range of sequence numbers

## Slide 100: Send Window & Receive Windows
Ws+Wr <=2n
Ws>=Wr
Ws,Wr<= 2n -1

## Slide 101: ACK Timer
ACK timer
  After an in-sequence data frame arrives, an auxiliary timer is started by start_ack_timer. If no reverse traffic has presented before this timer expires, a separate ACK frame is sent
  The timeout associated with the auxiliary timer be appreciably shorter than the timer used for timing out data frames

## Slide 102: NAK
Whenever the receiver has reason to suspect that an error has occurred, it sends NAK frame back to the sender
NAK frame is a request for retransmission
There are two cases when the receiver should be suspicious
  A damaged frame has arrived
  A frame other than the expected one arrived
To avoid making multiple requests for retransmission of the same frame, the receiver should keep track of whether a NAK has already been sent for a given frame

## Slide 103
Continued 

## Slide 104
Continued 

## Slide 105
Continued 

## Slide 107
3.5 Performance of Sliding Window Protocols

## Slide 108: Performance(1)
Stop-and-wait without error(transmission time=1,propagation=a)
a=tp/tf

## Slide 109: Performance(2)
Slide window without error

## Slide 110: Performance(3)
Stop-and-wait without error

## Slide 111: Performance(4)
Stop-and-wait without error

## Slide 112: Performance(5)
Stop-and-wait with error

## Slide 113: Performance(6)
Slide window without error

## Slide 114: Performance(7)
Piggybacking: U=N/(2+2a)

## Slide 115: Example
数据链路层采用GBN协议,发送方已经发送了编号为0-7的帧,当计时器超时时,若发送方只收到0,2,3号帧的确认,则发送方需要重发的帧数是?
数据链路层采用SR协议,发送方已经发送了编号为0-7的帧,当计时器超时时,若发送方只收到0,2,3号帧的确认,则发送方需要重发的帧数是?

## Slide 116: Example2
Consider a 50-kbps satellite channel with a 500-msec round-trip propagation delay, send 1000-bit frames
使用GBN协议,若使效率达到50%,序号的比特数至少是多少?
0.5=N/(1+2a)
a=250/(1000/50)=12.5

## Slide 117
3.6 Example Data Link Protocols

## Slide 118: Example Data Link Protocols
HDLC – High-Level Data Link Control
The Data Link Layer in the Internet
  SLIP (Serial Line IP)
  PPP (Point-to-Point Protocol)
PACKET over SONET
ADSL

## Slide 119
HDLC
(High-Level Data Link Control)

## Slide 120: History
IBM SDLC ,1974
  Synchronous Data Link Control
ANSI ADCCP
  Advanced Data Communication Control Procedure
ISO HDLC
  High-level Data Link Control
CCITT(ITU-T) LAPB
  LAP (Link Access Procedure)
  LAPB (Link Access Procedure – Balanced mode)

## Slide 121: HDLC Frame format
Frame format for bit-oriented protocols.

## Slide 122: HDLC Frames
Control field of
(a) An information frame. (I)
(b) A supervisory frame. (RR/RNR/REJ/SREJ)
(c) An unnumbered frame.(SABM,UA,DISC,FRMR)
First one or two bits of control filed identify frame type

## Slide 123: I-frame
If the first bit of the control field is 0, this means the frame is an I-frame.
3-bit N(S)
1-bit P/F
3-bit N(R)

## Slide 124: S-frame Control Field
If the first 2 bits of the control field are 10, this means the frame is an S-frame.
Code
  RR, RNR, REJ, SREJ (3-bit N(R))

## Slide 125: U-frame

## Slide 126: P/F Bit
Use depends on context
Unbalanced configuration
  Poll: Invite the terminal to send data
  Final: All the frames sent by the terminal, except the final one, have the P/F bit set to 0. The final one is 1
Balanced configuration
  Command (P bit): P=1 to solicit (poll) response from peer
  Response (F bit): F=1 indicates response to soliciting command
  Force the other machine to send a Supervisory frame immediately rather than waiting for reverse traffic onto which to piggyback the window information

## Slide 127: ACK Frame: RR & RNR
RR: Reveiver Ready
  ACK frame used to indicate the N(R) frame expected
  This frame is used when there is no reverse traffic to use for piggybacking
RNR: Reveiver Not Ready
  It acknowledges all frames up to but not including N(R) , just as RR does, but it tells the sender to stop sending (Flow control)

## Slide 128: NAK Frame: REJ & SREJ
REJ: Reject
  Indicate that a transmission error has been detected
  The N(R) field indicates the first frame in sequence not received correctly (i.e., the frame to be retransmitted)
  The sender is required to retransmit all outstanding frames starting at N(R)
SREJ: Selective Reject
  Calls for retransmission of only the frame specified by N(R)
  If a receiver wishes to buffer out-of-sequence frames for potential future use, it can force the retransmission of any specific frame using SREJ

## Slide 129: HDLC Station Types
Primary station
  Controls operation of link
  Frames issued are called commands
  Maintains separate logical link to each secondary station
Secondary station
  Under control of primary station
  Frames issued called responses
Combined station
  May issue commands and responses

## Slide 130: HDLC Link Configurations
Unbalanced
  One primary and one or more secondary stations
  Supports full-duplex and half-duplex
Balanced
  Two combined stations
  Supports full-duplex and half-duplex

## Slide 131: HDLC Operation
Exchange of information, supervisory and unnumbered frames
  Information - data to be transmitted to user (next layer up)
    Flow and error control piggybacked on information frames
  Supervisory - ARQ when piggyback not used
  Unnumbered - supplementary link control
Three phrases
  Initialization
  Data transfer
  Disconnect

## Slide 132: Example of HDLC Operation

## Slide 133: Example of HDLC Operation

## Slide 134
SLIP
(Serial Line IP)

## Slide 135: SLIP – Serial Line Internet Protocol
RFC1055
Framing: Character Stuffing
    Use 0xC0 as a flag char
    Use 0xDB 0xDC to replace 0xC0
    Use 0xDB 0xDB to replace 0xDB
Problems
    No error control
    Only support IP
    Don’t assign IP address dynamically
    No authentication
    Different version exist

## Slide 136
PPP
(Point to Point Protocol )

## Slide 137: The Data Link Layer in the Internet
A home personal computer acting as an internet host.

## Slide 138: PPP Protocol Sub-layers
PHYSICAL
LCP
NCP
PPP
IPCP
IPXCP
Others
IP
IPX
Third Layer

## Slide 139: Multiple protocols
PPP encapsulation
TCP/IP
Novell IPX
…...

## Slide 140: PPP - Point to Point Protocol
Protocol specifications:
  RFC1661,1662,1663
Features:
Layer 1
  Synchronous circuits (bit-oriented encodings)
  Asynchronous circuits (byte-oriented encodings)
  PPPoE (PPP over Ethernet, ADSL)
LCP: Link Control Protocol
  Error detection (CRC)
  Permits authentication
Allows IP addresses to be negotiated at connection time
Multiple protocols: NCP(IP, IPX, …)

## Slide 141: PPP Frame Format
The PPP full frame format for unnumbered mode operation.

## Slide 142: PPP Phase Diagram
A simplified phase diagram for bring a line up and down.

## Slide 143: LCP Frame Types
The LCP frame types.

## Slide 144: LCP Negotiates Protocol Options(1)
Max payload size for data frames(1500)
Authentication and choosing a protocol to use
  PAP：Password Authentication Protocol
  CHAP: Challenge Handshake Authentication Protocol
Line-quality monitoring during normal operation
Compression: Header and Data compression scheme
  Stacker
  Predictor
  Zlib

## Slide 145: LCP Negotiates Protocol Options(2)
CRC options
异步方式，字节填充法，指定转义字符集ACCM (Async-Control-Character-Map, 32 bits，用bitmap指定需转义的ASCII 码的控制字符集合)
  0x7E==>0x7D, 0x5E (0x7E为FLAG)
  0x7D==>0x7D, 0x5D
  控制字符C==> 0x7D，C xor 0x20 (C < 0x20)
Multilink Protocol (MP)
  ISDN (2B+D)

## Slide 146: CHAP Example
CHAP_REQUEST (Challenge-ID, server-name) 12618764(4-bytes Random), routerA
CHAP_RESPONSE (response, client-name) , Ty7ic#oM9@S...(16-bytes MD5), zhang
CHAP_SUCCESS/CHAP_FAILURE

## Slide 147: Packet over SONET
SONET
  the physical layer protocol that is used over the wide-area optical fiber links that make up the backbone of communications networks, including the telephone system.
  provides a bitstream that runs at a well-defined rate, for example 2.4 Gbps for an OC-48 link, some framing mechanism is needed.

## Slide 148: ADSL Protocol stacks
AAL5(ATM Adaptation Level 5)
  Framing and CRC
ATM
  ATM fixed-size cell (5-byte head and 48-byte payload)
ADSL physical layer
  Reed-Solomon code for error correction
  1-byte CRC, error detection
  DMT (Discrete MultiTone), QAM modulation