## Slide 1: 5 The Network Layer

## Slide 2: Highlights
Network Layer Design Issues
Routing Algorithms
Congestion Control Algorithms
Internetworking
IP

## Slide 3: Network Layer
Network Layer Design Issues
  Issues 
  Datagram 
  Virtual Circuit 
Routing Algorithms
  Shortest Path Routing 
  Flooding 
  Distance Vector Routing 
  Link State Routing 
  Hierarchical Routing 
Congestion Control Algorithms
  General Principles 
  Congestion Prevention 
  Congestion Control 
  Load Shedding
Quality of Service
Internetworking
Network Layer in the Internet
  Internet's Network Layer 
  IPv4 Header 
  ICMP 
  IP Addresses & Routing Table 
  NAT
  ARP,DHCP
  OSPF
  BGP 
  IPv6
HomeWork (1) (2)

## Slide 4: Overview
Network layer is the lowest layer that deals with end-to-end transmission
  Network layer must know about topology
  Avoid overloading some of the communication lines and routers while leaving others idle

## Slide 5: 5.1 Network Layer Design Issues

## Slide 6
Issues

## Slide 7: Network Layer Design Issues
Services Provided to Transport Layer
Internal Organization of Network Layer
Store-and-Forward Packet Switching

## Slide 8: Services Provided to Transport Layer
Design Goal
  The transport layer should be shielded from the number, type, and topology of the routers present
  The network addresses made available to the transport layer should use a uniform numbering plan, even across LANs and WANs
Two classes service
  Connection-Oriented Service (Virtual Circuit)
  Connectionless Service (Datagram)

## Slide 9
Datagram

## Slide 10: Datagram (1)
Routing within a datagram subnet

## Slide 11: Datagram(3)
A
1
2
3
4
5
B
C
B.3
B.2
B.1
C.3
C.2
C.1
B.3
B.2
B.1
C.3
C.2
C.1
C.3
C.1
C.2
B.1
B.3
B.2
A
B
C

## Slide 12
Virtual Circuit

## Slide 13: Virtual Circuit (1)
Routing within a virtual-circuit subnet.

## Slide 14: Virtual Circuit(2)
A
1
2
3
4
5
B
C
vc1
vc2
vc1: A--1--2--4--B
vc2: A--1--3--5--C
B.3
B2
B.1
C.3
C.2
C.1
C.3
C.2
C.1
B.3
B.2
B.1
A
B
C

## Slide 15: Virtual-Circuit vs. Datagram
5-4

## Slide 16: 5.2 Routing Algorithms

## Slide 17: Responsibility of Routing Algorithms
Responsible for deciding which output line an incoming packet should be transmitted on
  If the subnet uses datagrams internally, this decision must be made anew for every arriving data packet since the best route may have changed since last time
  If the subnet uses virtual circuits internally, routing decisions are made only when a new virtual circuit is being set up. Thereafter, data packets just follow the previously-established route (Session routing)
Forwarding & Routing

## Slide 18: Goals for the Routing Algorithm
Correctness
Simplicity
Robustness
Stability
Fairness
Optimality
  Minimizing mean packet delay
  Maximizing total network throughput

## Slide 19: Classification of Routing Algorithms
Nonadaptive algorithms (Static Routing)
  Do not base their routing decisions on measurements or estimates of the current traffic and topology
  The choice of the route to use is computed in advance, off-line, and downloaded to the routers when the network is booted
Adaptive algorithms
  Change their routing decisions to reflect changes in the topology, and usually the traffic as well

## Slide 20: The Optimality Principle
If router J is on the optimal path from router I to router K, then the optimal path from J to K also falls along the same route
  If a route rx better than r2 existed from J to K, it could be concatenated with r1 to improve the route from I to K
  Contradicting our statement that r1r2 is optimal
I
K
J
r1
r2
rx
r1+r2
？
r1+rx

## Slide 21: Sink Tree
  Optimal routes from all sources to a destination form a tree rooted at the destination
  Does not contain any loops, so each packet will be delivered within a finite number of hops
  The goal of routing algorithms
    Discover and use the sink trees for all routers
    Different routers may have different ideas about the current topology sometime

## Slide 22: Example of Sink Tree
(a) A subnet. (b) A sink tree for router B

## Slide 23
Shortest Path Routing

## Slide 24: Shortest Path Routing
Build a weighted and directed graph of subnet
  Nodes represent routers
  Arcs represents communication lines
Weight
  Hops
  Geographic distance in kilometers
  Mean queueing and transmission delay
    Determined by hourly test, some standard test packet
  A function of the distance, bandwidth, average traffic, communication cost, mean queue length, measured delay, and other factors
Dijkstra Algorithm
  Finds the shortest path between a given pair of routers

## Slide 25
Flooding

## Slide 26: Flooding
No network info required
Incoming packets retransmitted on every link except incoming link
Eventually a number of copies will arrive at destination
1
4
6
2
3
5

## Slide 27: Techniques for Damping the Flood
Problem
  Generates vast numbers of duplicate packets
    an infinite number unless some measures are taken to damp the process
Measures
  The header of each packet contains a hop counter
    Counter is decremented at each hop
    When the counter reaches zero, discard the packet
    Sender initializes the hop counter as the length of the path from source to destination, or the subnet diameter
  Source puts a sequence number in each packet
    Each router records maximal seq per source telling which seq have already been seen
  Selective flooding
    Each router records received data items in database
    Every data items contains a version number
    Olny new data items will be flooded

## Slide 28: Properties of Flooding
All possible routes are tried
  Very robust
At least one packet will have taken minimum hop count route
All nodes are visited
  Useful to distribute routing information

## Slide 29
Distance Vector Routing

## Slide 30: Distance Vector Routing
Each router maintains a table
  The best known distance to each destination
    The distance might be number of hops, time delay in milliseconds, …
  Which line to use
The table is updated by exchanging information with neighbors
  Send Routing information (Destination, Distance)
    Periodically (RIP Routing Information Protocol:30 seconds)
    Whenever table changes (triggered update)
  Receive Routing information
    Update local table if receive a better route
    Refresh existing routes
  Delete routing table items if they time out (RIP 180s)

## Slide 31: Example 1
Input from A, I, H, K, and the new routing table for J.

## Slide 32: Example 2: Initial Status
A
C
1
2
7
B
D
3
1
Dest. | Cost | NextHop
B | 2 | B
C | 7 | C
D | ∞ | -
Node A
Dest. | Cost | NextHop
A | 2 | A
C | 1 | C
D | 3 | D
Node B
Dest. | Cost | NextHop
A | 7 | A
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | NextHop
A | ∞ | -
B | 3 | B
C | 1 | C
Node D

## Slide 33: Example 2: 1st Iteration (C  A)
Dest. | Cost | NextHop
B | 2 | B
C | 7 | C
D | 8 | C
Node A
A
C
1
2
7
B
D
3
1
Dest. | Cost | NextHop
A | 2 | A
C | 1 | C
D | 3 | D
Dest. | Cost | NextHop
A | 7 | A
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | NextHop
A | ∞ | -
B | 3 | B
C | 1 | C
Node D
D(A, D) = D(A, C) + D(C,D) = 7 + 1 = 8
(D(C,A), D(C,B), D(C,D))
Node B

## Slide 34: Example 2: 1st Iteration (BA, CA)
Dest. | Cost | NextHop
B | 2 | B
C | 3 | B
D | 5 | B
Node A
A
C
1
2
7
B
D
3
1
Dest. | Cost | NextHop
A | 2 | A
C | 1 | C
D | 3 | D
Node B
Dest. | Cost | NextHop
A | 7 | A
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | NextHop
A | ∞ | -
B | 3 | B
C | 1 | C
Node D
D(A,D) = D(A,B) + D(B,D) = 2 + 3 = 5
D(A,C) = D(A,B) + D(B,C) = 2 + 1 = 3

## Slide 35: Example 2: End of 1st Iteration
A
C
1
2
7
B
D
3
1
Dest. | Cost | NextHop
B | 2 | B
C | 3 | B
D | 5 | B
Node A
Dest. | Cost | NextHop
A | 2 | A
C | 1 | C
D | 2 | C
Dest. | Cost | NextHop
A | 3 | B
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | NextHop
A | 5 | B
B | 2 | C
C | 1 | C
Node D
Node B

## Slide 36: Example 2: End of 2nd Iteration
A
C
1
2
7
B
D
3
1
Dest. | Cost | NextHop
B | 2 | B
C | 3 | B
D | 4 | B
Dest. | Cost | NextHop
A | 2 | A
C | 1 | C
D | 2 | C
Dest. | Cost | NextHop
A | 3 | B
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | NextHop
A | 4 | C
B | 2 | C
C | 1 | C
Node D
Node A
Node B

## Slide 37: Example 2: End of 3rd Iteration
A
C
1
2
7
B
D
3
1
Dest. | Cost | NextHop
B | 2 | B
C | 3 | B
D | 4 | B
Dest. | Cost | NextHop
A | 2 | A
C | 1 | C
D | 2 | C
Dest. | Cost | NextHop
A | 3 | B
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | NextHop
A | 4 | C
B | 2 | C
C | 1 | C
Node D
Nothing changes  algorithm terminates
Node A
Node B

## Slide 38: Count-to-infinity Problem

## Slide 39: Count-to-infinity Problem
B
C
1
1
A
D
1
“bad news travels slowly”
cost(B,A)= ∞
D | C | N
A | 1 | A
C | 1 | C
D | 2 | C
B
time
D | C | N
A | 2 | B
B | 1 | B
D | 1 | D
D | C | N
A | 3 | C
B | 2 | C
C | 1 | C
C
D
D | C | N
A | ∞ | -
C | 1 | C
D | 2 | C
D | C | N
A | 2 | B
B | 1 | B
D | 1 | D
D | C | N
A | 3 | C
B | 2 | C
C | 1 | C
D | C | N
A | 3 | C
C | 1 | C
D | 2 | C
D | C | N
A | 2 | B
B | 1 | B
D | 1 | D
D | C | N
A | 3 | C
B | 2 | C
C | 1 | C
D | C | N
A | 3 | C
C | 1 | C
D | 2 | C
D | C | N
A | 4 | B
B | 1 | B
D | 1 | D
D | C | N
A | 3 | C
B | 2 | C
C | 1 | C
D | C | N
A | 5 | C
C | 1 | C
D | 2 | C
D | C | N
A | 4 | B
B | 1 | B
D | 1 | D
D | C | N
A | 5 | C
B | 2 | C
C | 1 | C
D | C | N
A | 5 | C
C | 1 | C
D | 2 | C
D | C | N
A | 6 | B
B | 1 | B
D | 1 | D
D | C | N
A | 5 | C
B | 2 | C
C | 1 | C
D | C | N
A | 7 | C
C | 1 | C
D | 2 | C
D | C | N
A | 6 | B
B | 1 | B
D | 1 | D
D | C | N
A | 7 | C
B | 2 | C
C | 1 | C
…
Another problem:
cost(B,A): changed 1 to 4
cost(B,A): changed 4 to 1
RIP: Set infinity to 16

## Slide 40: Example

## Slide 41: Example

## Slide 42: Problem of Distance Vector Routing
Distance Vector Routing
  RIP (Routing Information Protocol)
  Cisco EIGRP (Enhanced Interior Gateway Routing Protocol)
The problem of Distance Vector algorithm
  When X tells Y that it has a path somewhere, Y has no way of knowing whether it itself is on the path
  Routed by rumor
Path Vector Routing
  BGP-4 (Border Gateway Protocol)
  IDRP (Inter-domain Routing Protocol)

## Slide 43
Link State Routing

## Slide 44: Link State Routing
Each router must do the following
  1. Discover its neighbors, learn their network address
  2. Set the distance or cost metric to each of its neighbors.（Measure the delay or cost to each of its neighbors）
  3. Construct a packet (LSP: Link-state Packet) telling all it has just learned
  4. Send LSP to all other routers (not only neighbors) reliably
  5. Compute the shortest path to every other router

## Slide 45: 1. Learning about the Neighbors
HELLO packet
  Broadcast network: Broadcast a special HELLO packet
  Multi-access network: Unicast HELLO to neighbors
Neighbors send back a reply telling who it is
  Names (Route IDs) must be globally unique
Simplify the topology
  When two or more routers are connected by a LAN or other multi-access network

## Slide 46: Artificial Node
(a) Nine routers and a LAN. (b) A graph model of (a)

## Slide 47: 2. Setting Link Costs
The cost to each of its neighbors
  The cost to reach neighbors can be set automatically
  Configured by the network operator
  Make the cost inversely proportional to the bandwidth of the link

## Slide 48: 3. Building Link State Packets
When to build LSP
  Build LSP periodically
  Build LSP when some significant event occurs
    such as a line or neighbor going down or coming back up again or changing its properties appreciably
(a) A subnet. (b) The link state packets for this subnet

## Slide 49: 4. Distributing the Link State Packets
Responsibility
  Distributing the LSP reliably
  Avoid different routers from using different versions of the topology, which can lead to inconsistencies, loops, unreachable machines, and other problems
The basic distribution algorithm
  Use flooding to distribute LSPs
  Guard against errors on the router-router lines, all LSP are acknowledged

## Slide 50: About Link State Packets
Sequence number
  If LSP is new, forwarded it on all lines except the one it arrived on
  If LSP is a duplicate, it is discarded (selective flooding)
  If lower than the highest one seen so far ever arrives, it is rejected as being obsolete
  If a router is down, and then restart, rejected
  if the sequence numbers wrap around, 32bit sequence number
  if a sequence number is ever corrupted, …
Age
  If a router is down
  If a router changed its routerID

## Slide 51: Refinements to LSP Flooding Algorithm

## Slide 52: 5. Computing the New Route
Once a router has accumulated a full set of LSPs, it can construct the entire graph
  Every link is represented twice, once for each direction. The two values can be averaged or used separately
Run Dijkstra's algorithm locally to construct the shortest path to all possible destinations
The results of this algorithm can be installed in the routing tables

## Slide 53
(a) 网络拓扑
局域网
L1
局域网
L2
2
2
5
4
4
3
3
3
2
8
8
13
12
12
10
7
6
16
A
B
H
G
F
E
C
D
I
广域网
W5
广域网
W3
广域网
W2
广域网
W6
广域网
W1
广域网
W4
A
(b) 有向图
L1
L2
W1
W3
W2
D
B
C
I
H
G
F
E
12
4
2
2
2
3
3
3
4
13
12
16
7
7
8
8
8
10
W4
W6
4
W5
6
5

## Slide 54
W3
A
有向图
L1
L2
W1
W2
D
B
C
I
H
G
F
E
12
4
2
2
2
3
3
3
4
13
12
16
7
7
8
8
8
10
W4
W6
4
W5
6
5
L1
L2
W1
W3
W2
D
B
A
I
G
F
E
4
3
3
12
16
7
8
8
W4
W6
W5
6
5
4
以路由器F为根的最短路径树
F
的
路
由
表
Dest | NextHop
L1 | D
L2 | G
W1 | D
W2 | D
W3 | (direct)
W4 | D
W5 | (direct)
W6 | G

## Slide 55: Examples of Link State Routing
IS-IS (Intermediate System-Intermediate System)
  DECnet
  ISO CLNP
  IP
  AppleTalk
  Novell NLSP (IPX)
  support multiple network layer protocols at the same time
OSPF (Open Shortest Path First)
  designed several years after IS-IS
  Only for IP

## Slide 56
Hierarchical Routing

## Slide 57: Hierarchical Routing (1)

## Slide 58: Hierarchical Routing (2)
Consider a subnet with 720 routers.
If there is no hierarchy
  720 routing table entries
If the subnet is partitioned into 24 regions of 30 routers each (Total:53)
  30 local entries
  23 remote entries
If a three-level hierarchy is chosen, with 8 clusters, each containing 9 regions of 10 routers (Total: 25)
  10 entries for local routers
  8 entries for routing to other regions within its own cluster
  7 entries for distant clusters

## Slide 59: 5.3 Congestion Control Algorithms

## Slide 60: Congestion
When too much traffic is offered, congestion sets in and performance degrades sharply
次要因素：突发流量与缓冲队列(太长/太短)
慢CPU忙于维护操作，转发操作太慢导致线路容量浪费

## Slide 61: Congestion Control & Flow Control
The difference between congestion control and flow control
  Congestion control is a global issue
  Flow control is to make sure that a fast sender cannot continually transmit data faster than the receiver is able to absorb it

## Slide 62: Approaches to Congestion Control
Network Provisioning
Traffic-aware routing
Admission Control
Traffic throtting
Load shedding

## Slide 63: Traffic-aware Routing
The normal routing schemes
  Used fixed link weights，adapted to changes in topology, but not to changes in load
Traffic-aware Routing
  Set the link weight to be a function of the link bandwidth and propagation delay plus the measured load or average queuing delay
  Danger： routing tables may oscillate wildly, leading to erratic routing and many potential problems
  If load is ignored and only bandwidth and propagation delay are considered, this problem does not occur
  In the Internet routing protocols do not generally adjust their routes depending on the load

## Slide 64: Traffic-aware Routing

## Slide 65: Admission Control
Widely used in virtual-circuit networks
  Do not set up a new virtual circuit unless the network can carry the added traffic without becoming congested
  Traffic descriptions: described in terms of its rate and shape (leaky bucket or token bucket)
  Can also be combined with traffic-aware routing by considering routes around traffic hotspots as part of the setup procedure

## Slide 66: Traffic Throttling (1)
When congestion is imminent, the net must tell the senders to throttle back their transmissions and slow down
Routers must determine when congestion is approaching, ideally before it has arrived
  the utilization of the output links
  the buffering of queued packets inside the router
  the number of packets that are lost
  平均值计算方法
EWMA (Exponentially Weighted Moving Average)
Routers must deliver timely feedback to the senders that are causing the congestion
  Choke packets
  ECN
  Hop-by-Hop backpressure

## Slide 67: Traffic Throttling (2)
Choke Packets
  router selects a congested packet and sends a choke packet back to the source, giving it the destination found in the packet
  （Internet SOURCE QUENCH message）
ECN(Explicit Congestion Notification)
  Router can tag any packet it forwards (by setting a bit in header) to signal that it is experiencing congestion
  When the net delivers the packet, the destination can note the congestion and inform the sender when it sends a reply packet
  The sender can then throttle its transmissions as before
  (Two bits in IP header are used to record whether the packet has experienced congestion)

## Slide 68: Traffic Throttling (3)
Hop-by-Hop Choke Packets
  Problem of sending a choke packet to the source
    High speed
    Over long distance
  Have the choke packet take effect at every hop it passes through
    Provide quick relief at the point of congestion at the price of using up more buffers upstream

## Slide 69: Hop-by-Hop Choke Packets
(a) A choke packet that affects only the source
(b) A choke packet that affects each hop it passes through

## Slide 70: Loading Shedding (1)
Loading Shedding
  When routers are being inundated by packets, just throw them away
Policies
  Wine & Milk
    E.g. file transfer, multimedia
  Requires cooperation from the senders
  Packet priority
    E.g. algorithms for compressing video, …
    The low-priority packets being cheaper to send than the high-priority ones, …
    Allow hosts to exceed the limits specified in agreement, but all excess traffic must be marked as low priority

## Slide 71: Loading Shedding (2)
RED (Random Early Detection)
  Drop packets before situation becomes hopeless
    When the average queue length on some line exceeds a threshold (be congested), action is taken
  How should router tell source about the problem?
    Send a choke packet
    Just discard the selected packet
  Sources respond to lost packets by slowing down their transmission rate
    Only works when sources respond to lost packets by slowing down their transmission rate
ECN & RED
  RED routers improve performance compared to routers that drop packets only when buffers are full
  ECN is the preferred option, it delivers a congestion signal explicitly rather than as a loss; RED is used when hosts cannot receive explicit signals

## Slide 72: 5.4 Quality of Service

## Slide 73: Four Primary Parameters
Reliability
Delay
Jitter
Bandwidth

## Slide 74: Requirements
5-30

## Slide 75: Traffic Shaping
Problem
  Host emits the packets irregularly, which may cause congestion to occur in network
Service Level Agreement (SLA)
  Between the user and the subnet
  The user: traffic shaping reduces congestion and helps carrier live up to its promise
  The carrier: traffic policing
  (CAR: Committed Access Rate)
Traffic shaping
  Regulate the average rate and burstiness of data transmission, smooth out the traffic
Traffic Policing
  Monitoring a traffic flow
  Packets in excess of the agreed pattern might be dropped or marked as having lower priority

## Slide 76: The Bucket Algorithm

## Slide 77: The Leaky Bucket Algorithm
Turns an uneven flow of packets into an even flow
  Smoothing out bursts
  Reducing the chances of congestion
Bucket can be used to shape or police packets entering the network
  If a packet arrives when the bucket is full， the packet must be queued until enough water leaks out to hold it （host shapes its traffic) or be discarded (network polices traffic)

## Slide 78: The Token Bucket Algorithm
Notes: 125*128/1000=16M 25*360/1000=9M
125*96/1000=12M,25*160=4M
25*1000/1000=25M

## Slide 79: Length of Maximum Rate Burst
burst length S sec
token bucket capacity B bytes
token arrival rate R bytes/sec
maximum output rate M bytes/sec
B + RS = MS
S = B/(M - R )
B=9600KB, M = 125 MB/s, R=25 MB/s
S=9600/(125 – 25)=96 ms
*突发速率为10Mbps的一台主机通过一个令牌桶进行流量调整。令牌桶的令牌到达速率为2Mbps，令牌桶的初始容量为8Mb。请问该主机以10Mbps速率可以传输多长时间？

## Slide 80: Packet Scheduling
Resources can be reserved for different flows
  Bandwidth
  Buffer space
  CPU cycles
Algorithms
  FIFO (FCFS), tail drop
  RED Algorithm
  Fair queueing algorithm

## Slide 81: Round-robin Fair Queueing
Problem
  It gives more bandwidth to hosts that use large packets than to hosts that use small packets

## Slide 82: WFQ: Weighted Fair Queueing
Ai: arrival time, Fi: finish time, Li: length of packet i
W: weight of the flow
Implementation complexity
  With N flows: O(logN) per packet

## Slide 83: 5.5 Internetworking

## Slide 84: How Networks Differ

## Slide 85: Connecting Different Networks
Two basic choices
  Build devices that translate or convert packets from each kind of network into packets
  Add a layer of indirection and building a common layer on top of the different networks (Cerf and Kahn, 1974)

## Slide 86: How Networks Can Be Connected

## Slide 87: Bridge & Router
Bridge: the entire frame is transported on the basis of its MAC address
Router: packet is extracted from the frame and the Layer-3 address is used for deciding where to send it

## Slide 88: Tunneling
Tunneling
  Source and destination hosts are on the same type of network, but there is a different network in between

## Slide 89: Internetwork Routing
(a)An internetwork. (b) A graph of the internetwork.
Interior gateway protocol (AS: Autonomous System)
Exterior gateway protocol

## Slide 90: MTU: Maximum Transmission Unit
Hardware (e.g., the size of an Ethernet frame)
Operating system (e.g., all buffers are 512 bytes).
Protocols (e.g., the number of bits in the packet length field)
Compliance with some (inter)national standard.
Desire to reduce error-induced retransmissions to some level
Desire to prevent one packet from occupying the channel too long

## Slide 91: Fragmentation
(a) Transparent fragmentation. (b) Nontransparent fragmentation.
(a) Recombination occurs at the exit gateway (ATM)
(b) Recombination occurs only at the destination host (IP)

## Slide 92: Transparent & Nontransparent Fragmentation
Transparent fragmentation
  Exit gateway must know when it has received all pieces
  All packets must exit via the same gateway.
  Overhead (reassemble and then re-fragment)
Nontransparent fragmentation
  Recombination occurs only at the destination host, it requires every host to be able to do reassembly，it requires routers to do less work
  When a large packet is fragmented, the total overhead increases because each fragment must have a header，a whole packet is lost if any of its fragments are lost, and fragmentation is more of a burden for hosts

## Slide 93: Numbering the Fragments (2)
Fragmentation when the elementary data size is 1 byte.
(a) Original packet, containing 10 data bytes.
(b) Fragments after passing through a network with maximum packet size of 8 payload bytes plus header.
(c) Fragments after passing through a size 5 gateway

## Slide 94: Solution of Getting Rid of Fragmentation
Path MTU discovery (Used in the modern Internet)
  Source: IP packet is sent with its header bits set to indicate that no fragmentation is allowed
  If a router receives a packet that is too large, it generates an error packet, returns it to source, and drops the packet
  When the source receives the error packet, it uses the information inside to refragment the packet into pieces that are small enough
  If a router further down the path has an even smaller MTU, the process is repeated.

## Slide 95: 5.6 The Network Layer in the Internet

## Slide 96: The Top 10 Principles (RFC1958 Clark)
Make sure it works
  Do not finalize the design or standard until multiple prototypes have successfully communicated with each other
Keep it simple
  If a feature is not absolutely essential, leave it out, especially if the same effect can be achieved by combining other features
Make clear choices
  If there are several ways of doing the same thing, choose one
Exploit modularity
Expect heterogeneity
Avoid static options and parameters
  If parameters are unavoidable (e.g., maximum packet size), it is best to have the sender and receiver negotiate a value than defining fixed choices
Look for a good design; it need not be perfect
Be strict when sending and tolerant when receiving
Think about scalability
Consider performance and cost

## Slide 97: The Internet's Network Layer
Vinton Cerf, Robert Kahn 1974, Turing Award 2004
The Internet: a Collection of Subnetworks (Autonomous Systems) that are interconnected
Its job is to provide a best-efforts way to transport datagrams from source to destination

## Slide 98
The IP Version 4 Protocol

## Slide 99: The IPv4 Header

## Slide 100: The IPv4 Header (1)
Version (4 bits)
IHL(4 bits)
  How long the header is, in 32-bit words, Val:5~15, 20~60 bytes
The Differentiated services field
  Originally, it was called the Type of service field （TOS）
    a 3-bit Precedence field: (Priority 0~7)
    3 flags: Delay, Throughput, Reliability
  Now, the top 6 bits are used to mark the packet with its service class the bottom 2 bits are used to carry explicit congestion notification (ECN) information
Total Length(16 bits)
  Includes both header and data, in bytes
  The maximum length is 65,535 bytes
  45 00 00 30

## Slide 101: The IPv4 Header (2)
Identification (16 bits)
  Allow the destination host to determine which datagram a newly arrived fragment belongs to
  All the fragments of a datagram contain the same Identification value
DF (1 bit)
  Don't Fragment. It is an order to the routers not to fragment the datagram (Originally, it was intended to support hosts incapable of putting the pieces back together again. Now it is used as part of the process to discover the path MTU)
MF (1 bit)
  More Fragments
Fragment offset (13 bits)
  Tell where in the current datagram this fragment belongs, in 8 bytes (0~8191)
  82 fc 40 00

## Slide 102: The IPv4 Header (3)
TTL: Time to live (8 bits)
  A counter used to limit packet lifetimes. It is supposed to count time in seconds
  It must be decremented on each hop
  When it hits zero, the packet is discarded and a warning packet is sent back to the source host
Protocol field (8 bits)
  Which transport process to give it to (TCP/UDP,…)
  1-ICMP, 6-TCP, 17-UDP,89-OSPF,
  50-AH,51-ESP,132-SCTP,...
The Header checksum (16 bits)
  Verifies the header only
  Must be recomputed at each hop
80 06 f5 a5
Source & Destination address(32+32 bits)
80 a8 b1 99
3b 40 6e d5

## Slide 103: Example
45 00 00 30
82 fc 40 00
80 06 f5 a5
80 a8 b1 99
3b 40 6e d5
06 64 31 ba 22 68 b9 90 00 00 00 00 70 02 ff ff ec e2 00 00
Notes: 128.168.177.153________59.64.110.213________

## Slide 104: Example2
45 00 00 30
00 00 40 00
40 06 b8 a2
3b 40 6e d5
80 a8 b1 99
31 ba 06 64 5b 9f f7 1c 22 68 b9 91 70 12 20 00 83 45 00 00

## Slide 105: Some of the IP options
Security option
Strict source routing option
  Gives the complete path from source to destination as a sequence of IP addresses
Loose source routing option
  Requires the packet to traverse the list of routers specified, and in the order specified, but it is allowed to pass through other routers on the way
Record route option
  Tells the routers along the path to append their IP address to the option field
The Timestamp option
  Like the Record route option, except that in addition to recording its 32-bit IP address, each router also records a 32-bit timestamp

## Slide 106: Example3

## Slide 107
IP Addresses

## Slide 108: Class A, B, C, and D formats
ICANN (Internet Corporation for Assigned Names and Numbers)

## Slide 109: Special IP addresses

## Slide 110: Prefixes
IP addresses are hierarchical
  Each 32-bit address is comprised of a variable-length network portion and a host portion
  The network portion has the same value for all hosts on a single network, a network corresponds to a contiguous block of IP address space (IP address block)
  Routers forward packets based on only the network portion of the address
128.208.0.0/24 (prefix length)
128.208.0.0/255.255.255.0 (netmask)

## Slide 111: Netmask and Prefix
/1 /2 /3 /4 /5 /6 /7 /8
192 224 240 248 252 254 255
/19 255.255.224.0

## Slide 112: Subnets
Outside the network, the subnetting is not visible

## Slide 113: Subnet
子网 | 分配地址数 | 网络地址 | 子网掩码
LAN1 | 95 |  | 
LAN2 | 76 |  | 
将IP地址空间192.168.1.0/24按网络号递增顺序分配给2个局域网LAN1～LAN2

## Slide 114: Subnet
子网 | 分配地址数 | 网络地址 | 子网掩码
LAN1 | 95 |  | 
LAN2 | 56 |  | 
LAN3 | 60 |  | 
将IP地址空间192.168.1.0/24按网络号递增顺序分配给3个局域网LAN1～LAN3

## Slide 115: CIDR—Classless InterDomain Routing
Route aggregation
  To reduce routing table sizes, combine multiple small prefixes into a single larger prefix
C 11000010 00011000 00000xxx xxxxxxxx
E 11000010 00011000 000010xx xxxxxxxx
(A) 11000010 00011000 000011xx xxxxxxxx
O 11000010 00011000 0001xxxx xxxxxxxx
C 11111111 11111111 11111000 00000000 255.255.248.0
E 11111111 11111111 11111100 00000000 255.255.252.0
(A) 11111111 11111111 11111100 00000000 255.255.252.0
O 11111111 11111111 11110000 00000000 255.255.240.0

## Slide 116: IP Address Assignments(Oxford subnet)
C 11000010 00011000 00000xxx xxxxxxxx (194.24.0.0-194.24.7.255)
E 11000010 00011000 000010xx xxxxxxxx (194.24.8.0-194.24.11.255)
A 11000010 00011000 000011xx xxxxxxxx (194.24.12.0-194.24.15.255)
O 11000010 00011000 00010xxx xxxxxxxx
O 11000010 00011000 000110xx xxxxxxxx
C 11000010 00011000 00000xxx xxxxxxxx (194.24.0.0-194.24.7.255)
E 11000010 00011000 000010xx xxxxxxxx (194.24.8.0-194.24.11.255)
A 11000010 00011000 000011xx xxxxxxxx (194.24.12.0-194.24.15.255)
O 11000010 00011000 0001xxxx xxxxxxxx (194.24.16.0-194.24.31.255)

## Slide 117: Aggregation of IP prefixes

## Slide 118: Longest matching prefix routing
Notes: Route-server.ip.att.net

## Slide 119: Routing Table
Routing table
  An array of (IP address, netmask, outgoing line, Next hop)
Scan the routing table
  Mask the destination address and comparing it to the table entry looking for a match
  It is possible that multiple entries (with different netmask lengths) match, in which case the longest mask is used
    If there is a match for a /20 mask and a /24 mask, the /24 entry is used.
Implementation
  Complex algorithms have been devised to speed up the address matching process
  commercial routers use custom VLSI chips with these algorithms embedded in hardware

## Slide 121: Routing
地址/掩码 | 下一跳
135.46.56.0/22 | 接口0
135.46.60.0/22 | 接口1
192.53.40.0/23 | 路由器1
默认(0.0.0.0/0) | 路由器2
(a) 135.46.63.10
(b) 135.46.57.14
(c) 135.46.52.2
(d) 192.53.40.7
(e) 192.53.56.7

## Slide 122: Routing Table

## Slide 123: Routing Table

## Slide 124
NAT

## Slide 125: NAT (Network Address Translation)
Outgoing packet
  10.x.y.z source address and TCP Source port are replaced
  Both the IP and TCP checksums are recomputed
Incoming packet
  Destination port =>internal IP address and original TCP Source port, Recompute IP and TCP checksums
  Deliver the packet using the 10.x.y.z address

## Slide 126: Private Network Address
The three reserved ranges
10.0.0.0 – 10.255.255.255/8 (Prefix 1.0B)
  00001010.xxxxxxxx.xxxxxxxx.xxxxxxxx
(16,777,216 hosts)
172.16.0.0 – 172.31.255.255/12 (Prefix 1.5B)
  10101100.0001xxxx.xxxxxxxx.xxxxxxxx
(1,048,576 hosts)
192.168.0.0 – 192.168.255.255/16 (Prefix 2.0B)
11000000.10101000.xxxxxxxx.xxxxxxxx
(65,536 hosts)
10.0.0.0/8, 172.16.0.0/12, 192.168.0.0/16

## Slide 127: 动态NAT表项
A：发送TCP报 10.0.0.1:3723->18.7.22.83:80
R：路由器动态创建NAT表项:
(Local)10.0.0.1:3723—(Global)123.116.156.133:33120—(Peer)18.7.22.83:80
改TCP报为123.116.156.133:33120->18.7.22.83:80
S：服务器S回数据18.7.22.83:80->123.116.156.133:33120
R：查NAT表：改TCP报为为18.7.22.83:80->10.0.0.1:3723
A：收到数据包18.7.22.83:80->10.0.0.1:3723
（连接过程中使用该NAT表项，当连接关闭时或长久未用的NAT表项，删除）
OUT: (SRC)10.0.0.1:3723—(DST)18.7.22.83:80=>(SRC)123.116.156.133:33120
IN: (SRC)18.7.22.83:80—(DST)123.116.156.133:33120=>(DST)10.0.0.1:3723
Notes: TABLE IN NAT ROUTER
-----------------------------------------------------
(Local) (Global) （Peer）
10.0.0.1:9900—123.116.156.133:1—18.7.22.83:80
10.0.0.2:9900—123.116.156.133:2—18.7.22.83:80
10.0.0.3:9900—123.116.156.133:3—18.7.22.83:80
…
10.0.255.255:9900—123.116.156.133:65535—18.7.22.83:80
10.1.0.1:9900—123.116.156.133:1—118.7.22.83:80
10.1.0.2:9900—123.116.156.133:2—118.7.22.83:80
10.1.0.3:9900—123.116.156.133:3—118.7.22.83:80
…
10.1.255.255:9900—123.116.156.133:65535—118.7.22.83:80
-------------------------------------------------------------
Item Example:
10.1.255.255:9900—123.116.156.133:65535—118.7.22.83:80
IP Packets:
PC->ROUTER: 10.1.255.255:9900->118.7.22.83:80
ROUTER->SERVER: 123.116.156.133:65535->118.7.22.83:80
SERVER->ROUTER: 118.7.22.83:80->123.116.156.133:65535
ROUTER->PC: 118.7.22.83:80->10.1.255.255:9900

## Slide 128: 静态NAT表项
R：设10.0.0.7为Web服务器: 建立静态NAT表
(Local)10.0.0.7:8080—(Global)123.116.156.133:80 —(Peer)*:*
C：因特网上的客户端C发送TCP数据包：
17.1.1.10:3598->123.116.156.133:80
R：查 NAT表，改为17.1.1.10:3598->10.0.0.7:8080
W：Web服务器回数据10.0.0.7:8080->17.1.1.10:3598
R：查 NAT表，改为123.116.156.133:80->17.1.1.10:3598
C：收到返回TCP数据报123.116.156.133:80->17.1.1.10:3598

## Slide 129: Some of the Objections to NAT
  NAT violates the architectural model of IP (IP地址不唯一标识一台计算机)
  NAT changes the Internet from a connectionless network to a kind of connection-oriented network
  NAT breaks the end-to-end connectivity model of the Internet (外网计算机无法主动发起向内网计算机的访问)
  NAT violates the most fundamental rule of protocol layering: layer k may not make any assumptions about what layer k + 1 has put into the payload field
  Processes on the Internet are not required to use TCP or UDP(无法支持非TCP/UDP)
  Some applications insert IP addresses in the body of the data
    FTP works this way

## Slide 130
IPv6

## Slide 131: IPv6: Major Goals
Address space
Reduce the size of the routing tables
Simplify the protocol, to allow routers to process packets faster
Security
Pay more attention to type of service, particularly for real-time data
Multicasting
Make it possible for a host to roam without changing its address
Allow the protocol to evolve in the future
Permit the old and new protocols to coexist for years

## Slide 132: The Main IPv6 Header

## Slide 133: The Main IPv6 Header
Address space
  128 bits, Total 3x1038
  7x1023 IP addresses per square meter on the Earth
IPv6 header has a fixed length
  The IHL field is gone
The Protocol field was taken out
Flow label
  Each flow is designated by the source address, destination address, and flow number
Fields relating to fragmentation were removed
  When a host sends a packet that is too large, the router sends back an error message
  This message tells the host to break up all future packets to that destination
Checksum field is gone

## Slide 134: The IPv6 Extension Headers

## Slide 135: IPv6 Address Notation
8 groups of 4 hexadecimal digits with colons between the groups
  8000:0000:0000:0000:0123:4567:89AB:CDEF
3 optimizations
  Leading zeros within a group can be omitted
  8000:0:0:0:123:4567:89AB:CDEF
  One or more groups of 16 zero bits can be replaced by a pair of colons
  8000::123:4567:89AB:CDEF
  IPv4 addresses can be written as a pair of colons and an old dotted decimal number
  ::192.31.20.46

## Slide 136
Internet Control Protocols

## Slide 137: ICMP (Internet Control Message Protocol)
ICMP message is encapsulated in an IP packet
DESTINATION UNREACHABLE
  a router cannot locate the destination
  a packet with the DF bit cannot be delivered because a ''small-packet'' network stands in the way
TIME EXCEEDED
  a packet is dropped because its TTL counter has reached zero
SOURCE QUENCH
  Choke packet：When a host received this message, it was expected to slow down
REDIRECT
  a router notices that a packet seems to be routed wrong
  It is used by the router to tell the sending host about the probable error
ECHO and ECHO REPLY
TIMESTAMP REQUEST and TIMESTAMP REPLY
The ROUTER ADVERTISEMENT and ROUTER SOLICITATION
  used to let hosts find nearby routers

## Slide 138: ICMP报文的格式
首 部
ICMP 报文
0
检验和
类型
代码
（这 4 个字节取决于 ICMP 报文的类型）
8
16
31
IP 数据报
前 4 个字节
都是一样的
ICMP 的数据部分（长度取决于类型）
ICMP报文分两类，即ICMP差错报告报文和ICMP询问报文
ICMP 报文的前4个字节是统一的格式，共有三个字段：即类型、代码和检验和。接着的4个字节的内容与ICMP的类型有关
数据部分

## Slide 139: ICMP差错报告报文的数据字段的内容
首部
IP 数据报
ICMP 的
前 8 字节
装入 ICMP 报文的 IP 数据报
IP 数据报
首部
ICMP 差错报告报文
8
字节
收到的 IP 数据报
IP 数据报
首部
8
字节
ICMP 差错报告报文
IP 数据报的数据字段

## Slide 140: ICMP的几种应用
traceroute
  利用TTL=0回送ICMP报文测路径，发TTL=1, =2, =3, ..., 的报文,回送ICMP报文的节点地址就是路径地址
主机分片
  以太网上主机TCP发送DF=1的1500字节IP报文经ADSL路由器MTU=1492,回ICMP报文报告MTU=1492,TCP重传并且后续发送报片长度均为1492
目的不可达
  主机TCP建连接，向远端网络未开机计算机发送IP报文，远端网络的路由器回ICMP报文报告主机不可达
路由重定向
  路由器收到IP报，转发，并用ICMP通告更好的转发路由器地址

## Slide 141: Windows tracert
d:\>tracert -d 202.108.33.89
Tracing route to 202.108.33.89 over a maximum of 30 hops
1 11 ms 3 ms 5 ms 118.207.192.1
2 5 ms 5 ms 2 ms 118.207.192.1
3 10 ms 6 ms 7 ms 124.205.97.48
4 4 ms 6 ms 2 ms 218.241.165.5
5 4 ms 3 ms 3 ms 218.241.165.9
6 5 ms 6 ms 5 ms 202.99.1.146
7 5 ms 12 ms 22 ms 124.207.222.26
8 20 ms 18 ms 31 ms 61.51.26.165
9 27 ms 18 ms 17 ms 211.154.208.189
10 22 ms 19 ms 17 ms 124.65.60.185
11 22 ms 27 ms 20 ms 61.148.152.5
12 16 ms 19 ms 27 ms 202.106.229.58
13 81 ms 18 ms 19 ms 210.74.178.198
14 20 ms 18 ms 23 ms 202.108.33.89
Trace complete

## Slide 142
ARP,DHCP

## Slide 143: 路由表，直接交付与间接交付

## Slide 144: ARP: Address Resolution Protocol
How do IP addresses get mapped onto data link layer addresses, such as Ethernet?
  A configuration file in the system that maps IP addresses onto Ethernet addresses
  A better solution is to output a broadcast packet onto the Ethernet asking: Who owns IP address 192.31.65.5?

## Slide 145
ARP 响应
A
Y
X
B
Z
B unicasts to A
ARP RESPONSE
A Broadcasts
ARP REQUEST
ARP 请求
ARP 请求
ARP 请求
ARP 请求
192.31.65.16
192.31.65.5
00-00-C0-15-AD-18
00-06-2B-00-EE-0A
我是 192.31.65.16，硬件地址是 00-00-C0-15-AD-18
我想知道主机 192.31.65.5的硬件地址
我是 192.31.65.5
硬件地址是 00-06-2B-00-EE-0A
A
Y
X
B
Z
192.31.65.16
192.31.65.5
00-00-C0-15-AD-18

## Slide 146: ARP: Optimizations
Source host: ARP cache
  Entries in the ARP cache should time out after a few minutes
Destination host:
  Records sender's (Ethernet address, IP address) pairs into cache
Other machines on the same Ethernet:
  Can enter the IP/MAC mapping in ARP REQUEST into their ARP caches
Gratuitous ARP: host broadcasts its IP/MAC when it boots, an ARP looking for its own IP address
  Side effect of the broadcast: make an entry in everyone's ARP cache
  If a response does (unexpectedly) arrive, two machines have been assigned the same IP address

## Slide 147: Proxy ARP
Host A send an IP datagram to Host B

## Slide 148: DHCP
DHCP (Dynamic Host Configuration Protocol)
  Allows both manual IP address assignment and automatic assignment (IP address, netmask, DNS server address, default gateway, file server, ......)
  In most systems, it has largely replaced RARP and BOOTP
  DHCP packet : DISCOVER/OFFER/REQUEST/ACK
  RFC 951,1084,1123,1533,1534,1497,1541
Leasing & renewal

## Slide 149: DHCP Client-Server Scenario
DHCP server: 223.1.2.5
Arriving
client
time
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
ipaddr: 0.0.0.0
transaction ID: 654
mac: 00-23-56-1e-dc-14
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
ipaddr: 223.1.2.4
transaction ID: 654
mac: 00-23-56-1e-dc-14
Lifetime: 3600 secs
DHCP request
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
ipaddr: 223.1.2.4
transaction ID: 655
mac: 00-23-56-1e-dc-14
Lifetime: 3600 secs
UDP is Used
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
ipaddr: 223.1.2.4
transaction ID: 655
mac: 00-23-56-1e-dc-14
Lifetime: 3600 secs

## Slide 150: DHCP Relay Agent

## Slide 151
OSPF (Open Shortest Path First)

## Slide 152: Routing Protocol
Interior Gateway Protocol
  RIP
  EIGRP (Security)
  OSPF (Security)
  IS-IS (Security)
Exterior gateway protocol
  BGP-4

## Slide 153: Example
AS-1
AS-2
AS-3
Interior router
BGP router

## Slide 154: OSPF: Requirements
Open (RFC 2328)
Dynamic algorithm: adapt to changes in the topology automatically and quickly
Support routing based on type of service
Load balancing, splitting the load over multiple lines
Hierarchical systems
Security

## Slide 155: 3 Kinds of Connections and Networks
Point-to-point lines between exactly two routers
Multi-access networks (How to find neighbors)
  Broadcasting (e.g., most LANs)
  Without broadcasting (e.g., most packet-switched WANs) NBMA
About Multi-access networks
  Designated router
  Neighboring routers that are not adjacent do not exchange information with each other
  The arcs from the network node to the routers have weight 0

## Slide 156: Link State Information

## Slide 157: OSPF Area
Divide AS into numbered ‘areas’
Every AS has only one backbone area, called area 0, all areas are connected to the backbone
Within an area, each router has the same link state database and runs the same shortest path algorithm
A router that connects to two areas needs the databases for both areas and must run the shortest path algorithm for each one separately

## Slide 158: Areas

## Slide 159: OSPF Routers
Internal routers
  Outside an area, its destinations are visible but not its topology
Area border Router (part of the backbone)
  Summarize the destinations in one area and inject this summary into the other. This summary includes cost info but no topology info (reduces traffic and simplifies the shortest-path computations)
  If there is only 1 router out of an area, routes to hosts out of the area always by the router (stub area)
AS boundary router
  Injects routes to external destinations on other ASes into the area, the external routes appear as destinations that can be reached via the AS boundary router
  An external route can be injected at one or more AS boundary routers

## Slide 160: 5 Types of OSPF Messages
OSPF messages are sent as raw IP packets (Proto 89)

## Slide 161: OSPF Messages
HELLO报文
  状态：Down -> Init -> 2-Way，选举DR和BDR
数据库描述（DD）报文
  两路由器初始化连接时交换链路状态数据库描述报文(仅用于描述而非实际传送链路-状态数据库内容)
链路-状态请求报文
  收齐DD报文之后，用这种报文请求相邻路由器链路状态数据库中的部分必要的数据，以达到拓扑结构信息同步
链路-状态更新报文
  把链路状态信息发给相邻节点
  邻接建立期间将用此报文回应“链路状态请求”报文的请求
  邻接关系维持期间，洪泛法散播链路状态信息也用这个报文
链路-状态应答报文
  可靠地分发LS信息，该报文是对“链路-状态更新报文”的ACK

## Slide 162
BGP (Border Gateway Protocol)

## Slide 163: BGP: Goals
Goals of an interior gateway protocol and an exterior gateway protocol
  All an interior gateway protocol has to do is move packets as efficiently as possible from the source to the destination
  IGP着重发现和计算路由，EGP控制路由的传播和选择最佳路由
Routing policies
  Typical policies involve political, security, or economic considerations
  Policies are typically manually configured into each BGP router (or included using some kind of script)
  They are not part of the protocol itself
From the point of view of a BGP router, the world consists of ASes and the lines connecting them

## Slide 164: Transit and Peering
Transit Service
Peering
  two ASes send routing advertisements to each other for the addresses that reside in their networks

## Slide 165: Propagation of BGP Route Advertisements
TCP connection between pairs of BGP routers
Path vector Protocol
  (Prefix, AS path, Next hop)

## Slide 166: How BGP Routers Choose Route
Detect and break routing loop
Routes via peered networks are chosen in preference to routes via transit providers
Shorter AS paths are better
Prefer the route that has the lowest cost within AS
  known as early exit or hot-potato routing
  It has the curious side effect of tending to make routes asymmetric

## Slide 167
MODEM