## Slide 1: 6 The Transport Layer

## Slide 2: Highlights
Transport service
Elements of transport protocols
  Addressing
  Connection
  Flow Control
Congestion control
The Transport Layer in Internet UDP/TCP
  connection management
  window management
  congestion management

## Slide 3: 6.1 The Transport Service

## Slide 4: The Transport Service
Transport layer is the heart of the whole protocol hierarchy
It provides reliable data transport end to end (ETE)
It masks the diversity of communication subnets, provide a common interface to the upper layer
  It fulfills the key function of isolating the upper layers from the technology, design, and imperfections of the subnet
It provides multiple SAPs sharing one network link

## Slide 5: The Transport Function
5
4
3
2
1
传输层提供应用进程间的逻辑通信
主机 A
主机 B
应用进程
应用进程
路由器 1
路由器 2
AP1
LAN2
WAN
AP2
AP3
AP4
IP 层
LAN1
AP1
AP2
AP4
端口
端口
5
4
3
2
1
IP 协议的作用范围
传输层协议 TCP 和 UDP 的作用范围
AP3

## Slide 6: Network, transport, application layers
There are two types of network service, connection-oriented and connectionless, there are also two types of transport service. If the transport layer service is so similar to the network layer service, why are there two distinct layers? Why is one layer not adequate?

## Slide 7: Nesting of segment, packet, and frame
TPDU（Transport Protocol Data Units ）= Segment

## Slide 8: Berkeley Sockets

## Slide 9: Client
int main()
{
int sock, bytes;
char buf[4096]; /* buffer for incoming file */
struct sockaddr_in server; /* Server’s SAP */
sock = socket(PF_INET, SOCK_STREAM, IPPROTO_TCP);
server.sin_family= AF_INET;
server.sin_addr.s_addr = inet_addr("192.168.0.176"); /* server’s address */
server.sin_port= htons(12345);
connect(sock, &server, sizeof(server));
write(sock, ”abc.txt”, 8);
/ * Go get the file and write it to standard output. */
for(;;) {
bytes = read(sock, buf, sizeof(buf)); /* read from socket */
if (bytes <= 0) exit(0); /* check for end of file */
write(1, buf, bytes); /* write to standard output */
}
}

## Slide 10: Server
int main()
{
int fd, sock, data_sock, bytes;
char buf[4096];
struct sockaddr_in server， peer;
server.sin_family = AF_INET;
server.sin_addr.s_addr = htonl(INADDR_ANY);
server.sin_port = htons(12345);
sock = socket(AF_INET, SOCK_STREAM, IPPROTO_TCP);
bind(sock, &server, sizeof(server));
listen(sock, 5);
for(;;) {
data_sock = accept(sock, &peer, sizeof(peer)); /* block for connection request */
read(data_sock, buf, sizeof(buf)); /* read file name from socket */
fd = open(buf, O_RDONLY); /* open the file to be sent back */
for(;;) {
bytes = read(fd, buf, sizeof(buf)); /* read from file */
if (bytes <= 0) break; /* check for end of file */
write(data_sock, buf, bytes); /* write bytes to socket */
}
close(fd); /* closefile */
close(data_sock); /* close connection */
}
}

## Slide 11: 6.2 Elements of Transport Protocols

## Slide 12: Transport Protocol & Data Link Protocol
Both have to deal with error control, sequencing, flow control
Environment differences
  Addressing of destinations
  Initial connection establishment
  Storage capacity in the subnet
  Allocation of buffers
  a large and varying number of connections with bandwidth that fluctuates as the connections compete with each other

## Slide 13: Elements of Transport Protocols
Addressing
Connection Establishment
Connection Release
Flow Control and Buffering

## Slide 14
Addressing

## Slide 15: Addressing
TSAPs, NSAPs and transport connections.

## Slide 16: Addressing
Gets the Server’s TSAP
  Well-known TSAP
  Look up a name server or directory server
Process server
  If there are many server processes, most of which are rarely used, it is wasteful to have each of them active (inetd)

## Slide 17: Process Server

## Slide 18
Connection Establishment

## Slide 19: Problem
Establishing a connection sounds easy
  One sends a CONNECTION REQUEST TPDU to the destination and wait for a CONNECTION ACCEPTED reply
Problems
  Network can lose, store, and duplicate packets
  The connection establishment TPDU could be delayed or duplicated

## Slide 20: Solution
Using throwaway transport addresses
Giving each connection a ID, but a crashed machine can not know which identifier have been used
Each connection starts numbering its segments with a different initial sequence number (the low-order k bits of the clock)
  Require transport entities to be idle for T sec after a recovery to let all old segments die off
  Prevent sequence numbers from being reused for a time T before their potential use as initial sequence numbers

## Slide 21: The Three-way Handshake
Three protocol scenarios for establishing a connection using a three-way handshake
(a) Normal operation
(b) Old CONNECTION REQUEST appearing out of nowhere
(c) Duplicate CONNECTION REQUEST and duplicate ACK
CR: Connect Request

## Slide 22
Connection Release

## Slide 23: Two Styles
Asymmetric Release (violent)
  when one party hangs up, the connection is broken
  Asymmetric release is abrupt and may result in data loss
Symmetric Release (graceful)
  Treats connection as two separate unidirectional connections
  Requires each one to be released separately
CR: Connect Request

## Slide 24: The Two-army Problem

## Slide 25: Connection Release
(a) Normal case of a three-way handshake. (b) final ACK lost.
Releasing a connection means
  The transport entity removes the information about the connection from its table of currently open connections and signals the connection's owner (the transport user) somehow
(Disconnect Request)

## Slide 26: Connection Release
(c) Response lost (d) Response lost and subsequent DRs lost

## Slide 27: Connection Release: Half-open Connections
Half-open connection
  if the initial DR and N retransmissions are all lost. The sender will give up and release the connection, while the other side knows nothing at all about the attempts to disconnect
Kill off half-open connections
  If no TPDUs have arrived for a certain number of seconds, the connection is then automatically disconnected
  Dummy TPDU: just to keep the other side from disconnecting (keepalive, heartbeat)

## Slide 28
Error Control
and Flow Control

## Slide 29: Error Control
Error-detecting code (e.g., a CRC or checksum)
ARQ (Automatic Repeat reQuest)：
  Stop-and-wait
  sliding window protocol

## Slide 30: Source Buffering & Destination Buffering
The optimum buffering between source buffering and destination buffering
  Buffering at sender
  Buffering at receiver
Variable sized windows: Dynamic buffer management
  The sender and receiver need to dynamically adjust their buffer allocations
  The receiver piggybacks both acknowledgements and buffer allocations onto the reverse traffic
  Decouple buffering from acknowledgments

## Slide 31: Buffer Size Problem
(a) Chained fixed-size buffers. (b) Chained variable-sized buffers. (c) One large circular buffer per connection.

## Slide 32: Dynamic buffer allocation

## Slide 33: Flow Control
Two flow control factor
  Buffer space available in the receiver
    explicit window indication
  The capacity of the subnet
    sender monitor the network’s carrying capacity

## Slide 34: Multiplexing
(a) Multiplexing. (b) Inverse multiplexing(SCTP)

## Slide 35: 6.3 Congestion Control

## Slide 36
Desirable Bandwidth Allocation

## Slide 37: Congestion Control
Responsibility of the network and transport layers
  Congestion occurs at routers, so it is detected at the network layer
  The only effective way is for the transport protocols to send packets into the network more slowly
Internet relies heavily on the transport layer for congestion control (TCP)
Goal of Congestion Control Algorithm
  Avoid congestion
  Find a good allocation of bandwidth to use all the available bandwidth (Efficiency)
  Be fair across competing transport entities (Fairness)
  Quickly track changes in traffic (Convergence)

## Slide 38: Efficiency and Power
The load with the highest power represents an efficient load for the transport entity to place on the network

## Slide 39: Max-Min Fairness
How to divide bandwidth between transport senders
  Networks do not have a strict bandwidth reservation for each flow or connection
  IP routers often have all connections competing for the same bandwidth
Max-min fairness
  If the bandwidth given to one flow cannot be increased without decreasing the bandwidth given to another flow with an allocation that is no larger

## Slide 40: Examples

## Slide 41: Convergence
Converge quickly to a fair and efficient allocation of bandwidth
  The ideal operating point for the network varies over time
  The algorithm should rapidly converge to the ideal operating point, and it should track that point as it changes over time

## Slide 42
Regulating the Sending Rate

## Slide 43: Sending Rate Limited by 2 Factors
Flow control & Congestion

## Slide 44: Feedback from Network
If an explicit and precise signal is given
  Use the signal to adjust rate to the new operating point
In the other cases (the control law)
  No congestion signal, senders should increase their rates
  When a congestion signal is given, senders should decrease their rates

## Slide 45: Additive and Multiplicative Bandwidth Adjustments

## Slide 46: AIMD Control Law
AIMD(Additive Increase Multiplicative Decrease) does converge to optimal point both fair and efficient

## Slide 47: AIMD is Used by TCP
Not adjusting the rate directly, a strategy used in practice is to adjust the size of a sliding window
  If the window size is W and the round-trip time is RTT, the equivalent rate is W/RTT
  Be easy to combine with flow control, which already uses a window, and has the advantage that the sender paces packets using acknowledgements
  Not quite fair: different connections have different RTTs, this leads to a bias in which connections to closer hosts receive more bandwidth than connections to distant hosts
TCP-friendly congestion control in non-TCP transport protocols
  There is significant community pressure for new transport protocols to be designed so that they compete fairly with TCP

## Slide 48: 6.4 The Internet Transport Protocols

## Slide 49
UDP
(User Datagram Protocol)

## Slide 50: The Internet Transport Protocols
TCP (Transmission Control Protocol)
  RFC793
  Connection-oriented protocol
  Byte-stream
UDP (User Datagram Protocol)
  RFC768
  Connectionless Protocol
TCP/IP Protocol Stack
Application
TCP UDP
Host-to-Network
IP

## Slide 51: UDP (User Datagram Protocol)
Does not do flow control, error control, or retransmission upon receipt of a bad segment
Provide an interface to the IP protocol with the added feature of demultiplexing multiple processes using the ports
Broadcast & Multicast
User datagram boundary

## Slide 52: UDP Header
Checksum
  Optional: Stored as 0 if not computed (a true computed 0 is stored as all 1s)
  The checksum algorithm is simply to add up all the 16-bit words in one’s complement and to take the one’s complement of the sum
  Including header、data and the pseudoheader in the UDP checksum computation helps detect misdelivered packets

## Slide 53: UDP Checksum
伪首部
源端口
目的端口
长 度
检验和
数 据
首 部
UDP长度
源 IP 地址
目的 IP 地址
0
17
IP 数据报
字节
4
4
1
1
2
12
2
2
2
2
字节
发送
数 据
首 部
UDP 用户数据报

## Slide 54: UDP Applications
DNS (Domain Name System)
DHCP (Dynamic Host Configuration Protocol)
RIP (Routing Information Protocol)
RTP (Real-time Transport Protocol)
TFTP (Trivial File Transfer Protocol)
RPC (Remote Procedure Call)
NFS (Net File System)
P2P (Peer-to-Peer, DHT, ‘Kademlia’)

## Slide 55
TCP
(Transmission Control Protocol)

## Slide 56: The TCP Service Model
Socket
  socket address: IP address and Port (16-bit, TSAP)
  Each connection is identified by a pair of sockets
Well-known ports
  Reserved for standard services
  RFC1700
  ‘inetd’ process (Internet daemon)
TCP connection
  Full-duplex
  End-to-End
    TCP does not support multicasting or broadcasting
  Byte-stream, not message stream (Why?)
    Message boundaries are not preserved end to end, just like UNIX file

## Slide 57: TCP Well-known ports

## Slide 58: TCP Byte-stream
(a) Four 512-byte segments sent as separate IP datagrams.
(b) The 2048 bytes of data delivered to the application in a single READ CALL
PUSH flag
  To force data out, applications can use the PUSH flag, which tells TCP not to delay the transmission
Urgent data

## Slide 59: TCP Segment Header

## Slide 60: TCP Protocol (1)
TCP Entity
  A port plus its host's IP address forms a 48-bit unique end point
  The source and destination end points together identify the connection
  (Local IP, Local port, Peer IP, Peer Port)
32-bits sequence
  Count byte, not segment (network speeds ，56k/1week)
  sequence numbers, acknowledgements number
  TCP sender can accumulate data from several writes into one segment or can split data from one write over multiple segments
  The retransmissions may include different byte ranges than the original transmission

## Slide 61: TCP Protocol (2)
TCP Segment
  20 or more bytes head, n bytes data
  Segments without any data are legal and are commonly used for ACK and control messages
MSS (Maximum Segment Size)
  Limited by IP datagram length
  Limited by MTU of each data link, so router could fragment a segment
Variable sized sliding window
Reorder the segment
  Disordered and duplicated segments received by the receiver

## Slide 62: The TCP checksum
The pseudoheader included in the TCP checksum
TCP Checksum
  It checksums the header, the data, and the conceptual pseudoheader
  Pseudoheader: helps detect misdelivered packets
  Checksum is mamdatory

## Slide 63: TCP Options
MSS option
  Allow hosts to specify the maximum TCP payload it is willing to accept
  During connection setup, each side can announce its maximum and see its partner's
  If a host does not use this option, it defaults to a 536-byte payload
  The maximum segment size in the two directions need not be the same
Window scale option
  Allow the sender and receiver to negotiate a window scale factor
Selective repeat instead of go back n protocol
  NACK: RFC 1106 introduced NAKs to allow the receiver to ask for a specific segment
  Selective Acknowledgment (SACK)
  Timestamp option
  The PAWS (Protection Against Wrapped Sequence numbers)

## Slide 64
Notes: ————
Kind
(Type)
Length
Name
Reference
描述 & 用途
0
1
EOL
RFC 793
选项列表结束
1
1
NOP
RFC 793
无操作（用于补位填充）
2
4
MSS
RFC 793
最大Segment长度
3
3
WSOPT
RFC 1323
窗口扩大系数（Window Scaling Factor）
4
2
SACK-Premitted
RFC 2018
表明支持SACK
5
可变
SACK
RFC 2018
SACK Block（收到乱序数据）
8
10
TSPOT
RFC 1323
Timestamps
19
18
TCP-MD5
RFC 2385
MD5认证
28
4
UTO
RFC 5482
User Timeout（超过一定闲置时间后拆除连接）
29
可变
TCP-AO
RFC 5925
认证（可选用各种算法）
253/254
可变
Experimental
RFC 4727
保留，用于科研实验

## Slide 65: TCP Connection Establishment
Client
  Executes a CONNECT primitive, specifying the IP address and port, sends a TCP segment with the SYN bit on and ACK bit off and waits for a response
Server
  When client’s SYN segment arrives, checks to see if there is a process that has done a LISTEN on the port
    If not, it sends a reply with the RST bit on to reject the connection
    If some process is listening to the port, that process is given the incoming TCP segment, ......

## Slide 66: TCP Connection Establishment
(a) TCP connection establishment in the normal case.
(b) Simultaneous connection establishment on both sides.

## Slide 67: Initial Sequence Number
Initial sequence number
  A clock-based scheme is used, with a clock tick every 4 µsec
When a host crashes
  It may not reboot for the maximum packet lifetime to make sure that no packets from previous connections are still roaming around the Internet somewhere

## Slide 68: TCP Connection Release
Host 1
Host 2
FIN=1, Seq=x
Ack= x+1
Application request releasing connection
Notify application
Application request releasing connection
Notify application
FIN=1, Seq= y
Ack= y+1
Release the whole connection
Use timer to avoid the two-army problem
  If a response to a FIN is not forthcoming within two maximum packet lifetimes, the sender of the FIN releases the connection

## Slide 69: TCP Connection Management Modeling
States used in the TCP connection management finite state machine

## Slide 70: TCP Finite State Machine

## Slide 71: TCP Finite State Machine

## Slide 72: TCP Connection Establishment

## Slide 73: TCP Connection Release (1)

## Slide 74: TCP Connection Release(2)

## Slide 75: TCP Connection Release (3)

## Slide 76: Window management in TCP

## Slide 77: Window management in TCP
When the window is 0
  Sender may not normally send segments
  Urgent data may be sent
  Sender may re-send a 1-byte segment to probe ACK & window to prevent deadlock

## Slide 78: Nagle’s algorithm
Problem
  Overhead: TCP head + IP head=20+20 bytes
  When used in TELNET connection, 1 data bytes carried with 40 bytes overhead
  (41+40+40+41)(DATA+ACK+WIN+ECHODATA)
Improvement algorithm
  Receiver: Delay acknowledgement and window update, reduce the load placed by the receiver
  Sender: Nagle’s algorithm
  Send one segment unless either of the following condition exist:
    Acknowledgement to last segment has been received
    Buffered data fills half the window or a maximum segment
TCP Option
  TCP_NODELAY: Disable Nagle’s algorithm & using PUSH bit
  Linux TCP_CORK: Disable Nagle’s algorithm, wait 200ms to accumulate data for sending

## Slide 79: Silly Window Syndrome
Clark’s solution
Receiver should not send a window update until it can handle the MSS or its buffer is half empty, whichever is smaller

## Slide 80: Other TCP Policies
Receiver
  Buffers received data, blocks a READ request from the application until it has a large chunk of data to provide
  About out-of-order segments

## Slide 81: TCP Timer Management
(a) Probability density of ACK arrival times in the data link layer.
(b) Probability density of ACK arrival times for TCP.

## Slide 82: Retransmission Timer: Jacobson Algorithm
Solution
  Use a dynamic algorithm that adjusts the timeout interval, based on continuous measurements of network performance
Jacobson’s Algorithm
  R: How long the successful acknowledgement took
  α: A smoothing factor, typically α = 7/8.
  RTT: Estimate of the round-trip time
  RTT= αRTT+(1-α)R
  Timeout interval
  Timeout = β RTT , Typically β=2
Enhanced Algorithm
  Problem: a constant value was inflexible because it failed to respond when the variance went up
  Mean deviation (a cheap estimator of the standard deviation)
  RTTVAR= β RTTVAR +(1- β)|RTT-R|, Typically β =3/4
  Timeout interval
  Timeout = RTT+4 RTTVAR
    less than 1% packets come in more than four standard deviations late

## Slide 83: Estimate of RTT
  RTT= αRTT+(1-α)M, α=7/8
0 | 12.5% | 12.5%
1 | 10.9% | 23.4%
2 | 9.6% | 33.0%
3 | 8.4% | 41.4%
4 | 7.3% | 48.7%
5 | 6.4% | 55.1%
6 | 5.6% | 60.7%
7 | 4.9% | 65.6%
8 | 4.3% | 69.9%
9 | 3.8% | 73.7%
10 | 3.3% | 77.0%
11 | 2.9% | 79.9%
12 | 2.5% | 82.4%
13 | 2.2% | 84.6%
14 | 1.9% | 86.5%
15 | 1.7% | 88.2%
16 | 1.5% | 89.7%
17 | 1.3% | 91.0%
18 | 1.1% | 92.1%
19 | 1.0% | 93.1%
20 | 0.9% | 93.9%
21 | 0.8% | 94.7%
22 | 0.7% | 95.4%
23 | 0.6% | 95.9%
24 | 0.5% | 96.5%
25 | 0.4% | 96.9%
26 | 0.4% | 97.3%
27 | 0.3% | 97.6%
28 | 0.3% | 97.9%
29 | 0.3% | 98.2%

## Slide 84: Example RTT estimation (fr-usa)

## Slide 85: Retransmission Timer: Karn’s algorithm
Problem
  If a segment times out and is sent again, when ACK comes in, it is unclear whether the ACK refers to the first transmission or a later one. Guessing wrong can seriously contaminate the estimate of RTT
Karn’s algorithm
  Do not update RTT on any segments that have been retransmitted, instead, the timeout is doubled on each failure until the segments get through the first time

## Slide 86: Other TCP Timer
Persistence timer
  It is designed to prevent the 0-window deadlock
  When timer goes off, the sender transmits a probe to the receiver. The response to the probe gives the window size
Keepalive timer
  It is designed to prevent the half-open connection
  When a connection has been idle for a long time, the keepalive timer may go off to cause one side to check whether the other side is still there
The timer used in the TIMED WAIT state
  Avoid the two-army problem
  It runs for twice the maximum packet lifetime to make sure that when a connection is closed, all packets created by it have died off

## Slide 87
TCP Congestion Control

## Slide 88: Network capacity and Receiver capacity
(a) A fast network feeding a low capacity receiver
(b) A slow network feeding a high-capacity receiver

## Slide 89: TCP Congestion Control
Problem
  Starting in 1986, the growing popularity of Internet led to the first occurrence of congestion collapse
  New TCP software included congestion control should be able to work with the existing implementation, without changing any of the message formats
Van Jacobson’s Solution
  To approximate an AIMD congestion window
  TCP maintains a congestion window (cwin) and a flow control window, both are tracked dynamically, the sender window is the smaller of them
  Using packet loss as a congestion signal
    Depends on transmission errors being relatively rare
    This is why 802.11 includes its own retransmission mechanism
  A good timer is needed to detect packet loss accurately
    The timer includes estimates of the mean and variation in RTT

## Slide 90: Two Problems in Practice
  The way packets are sent into the network
    Must be matched to the network path, otherwise the traffic will cause congestion
  Consider a host with a window of 64 KB attached to a 1-Gbps Ethernet, if the host sends the entire window at once, the burst takes 0.5ms, but clogs a 1-Mbps ADSL line in the path for 500ms
The initial congestion windows size
  Consider a 10Mbps path with an RTT of 100ms, cwin should be the bandwidth-delay product, 100 packets of 1250 bytes
  If cwin starts at 1 packet, increases by 1 packet/RTT, it will be 100 RTTs (10s) before running at the right rate
  If starts with a larger initial window, say of 50 packets, the window would be far too large for slow or short links

## Slide 91: ACK Clock
Using the ACK clock
  The times for the ACKs reflect the times at which the packets arrived at the receiver after crossing the slow link
  As the ACKs travel over the net and back to the sender, they preserve this timing
  If TCP injects packets at the rate of ACKs returned, packets will be sent as fast as the slow link permits, they will not queue up and congest any router along the path
  By using an ACK clock, TCP smoothes out traffic and avoids unnecessary queues at routers.

## Slide 92: Slow Start
Slow Start
  When a connection is established, the cwin is initialized to a value of 1 or 4 segments
  The sender sends the initial window, packets will take a RTT to be acknowledged
  For each ACK, adds one segment to the cwin (exponential growth)
Performance
  Slow-start works well over a range of link speeds and round-trip times, and uses an ack clock to match the rate of sender transmissions to the network path

## Slide 93: Slow Start from an Initial Congestion Window of One Segment

## Slide 94: Slow Start Threshold
TCP connection maintains a threshold to keep slow start under control
  Initially, set the threshold as the size of the flow control window, set cwin as 1 or 4 segments
  TCP keeps increasing the cwin in slow start until a timeout occurs or the cwin exceeds the threshold
    Whenever a packet loss is detected, the threshold is set to be half of the cwin and the process is restarted
    Whenever the slow start threshold is crossed, TCP switches from slow start mode to additive increase mode

## Slide 95: Additive Increase Mode
The cwin is increased by one segment every round-trip time
  This is usually implemented with an increase after all segments in cwin is acknowledged
  Call the maximum segment size MSS, an approximation is to increase cwnd by (MSS×MSS)/cwnd for each of the cwnd/MSS packets

## Slide 96: Additive Increase from an Initial Congestion Window of One Segment

## Slide 97: Fast Retransmission
A quick way for the sender to recognize that one of its packets has been lost
  As packets beyond the lost packet arrive at the receiver, they trigger ACKs. These ACKs have the same ACK number
  If the sender receives a duplicate ACK, it is likely that another packet has arrived at the receiver. TCP assumes that 3 duplicate ACKs imply that a packet has been lost
  This packet is retransmitted before timeout, the threshold is set to half of the current cwin, slow start can be restarted by setting the cwin to 1 segment (just as a timeout)

## Slide 98: TCP Tahoe
Slow start followed by additive increase in TCP Tahoe

## Slide 99: Fast Recovery
Avoid slow start
  Set the new threshold as half of the current cwin at the time of the fast retransmission
  Duplicate ACKs are counted until the number of packets in the network has fallen to the new threshold
  From then on, a new packet can be sent for each duplicate ACK that is received
  One RTT after, the lost packet has been ACKed, the stream of duplicate ACKs ceases and fast recovery mode is exited
  Set cwin as the threshold and grows by linear increase (additive increase mode)
The upshot of fast-recovery algorithm
  Avoids slow start, except when the connection is first started and when a timeout occurs
  The cwin of a running connection follows a sawtooth pattern. That’s AIMD.

## Slide 100: TCP Reno
Fast recovery and the sawtooth pattern of TCP Reno

## Slide 101: TCP option: SACK
SACK (Selective ACKnowledgements)
  When TCP connection is set up, both the sender and receiver send the SACK permitted TCP option to signal that they understand SACK
  SACK lists up to 3 ranges of bytes that have been received
  (SACK is now widely deployed)

## Slide 102: TCP option: ECN
ECN Option
  ECN is enabled when both the sender and receiver indicate that they are capable of using ECN by setting the ECE and CWR bits during connection establishment
  The TCP receiver is informed if any packet that arrives carries an ECN congestion signal, it then uses the ECE (ECN Echo) flag to signal the TCP sender
  The sender tells the receiver that it has heard the signal by using the CWR (Congestion Window Reduced) flag
  The sender reacts to these notifications in exactly the same way as it does to packet loss that is detected via duplicate ACKs (multiplicative decrease)
(ECN is an IP layer mechanism, it requires both host and router support and is not yet widely used on the Internet)

## Slide 103: Various Implementations of TCP
TCP Tahoe (Van Jacobson, 1988)
TCP Reno (1990, 4.3 BSD) has formed the basis for TCP congestion control for more than two decades
Variants
  NewReno: recovering from two or more losses in a window
    Partial ACK: acknowledges some but not all of the packets that were outstanding at the start of Fast Recovery
  Linux 2.6 uses a variant called CUBIC TCP
  Windows includes a variant called Compound TCP
Selective ACK & TCP with ECN